## Slide 1
FEED FROM
TK-101
4"-P-101
V-101
P-100A
NRV-101
V-103
V-102
P-100B
NRV-102
V-104
PI
001
PI
002
3"-P-102
E-100
FEED PREHEATER
HEATING FLUID
FROM UNIT A
3"-HF-401
V-401
HV-063
TI
063
V-402
HF RETURN
TO UNIT A
DR
V-109 LC
INLET V-110 CSO
PSV-101
SET 1700 kPa g
TO SAFE LOC.
3"-P-103
TI
010
FE-008
FT
008
FIAL
008
FSLL
008
FIC
003
V-105
FV-010 FO
V-106
V-107 (BYPASS)
VENT
V-108 NC
3"-P-103
PI
009
TI
020
FLUE GAS TO ATMOSPHERE
HV-400 FO
HIC
400
AI
026
CO
PI
032
TI
021
AI
029
O₂
STACK
CONVECTION SECTION
PI
031
3"-P-104
TI
022
H-100
FIRED HEATER
NATURAL DRAFT, ONE OIL BURNER
RADIANT SECTION (FIREBOX)
RADIANT COIL
(NOTE 6)
BURNER
WINDBOX
PI
003
TIAH
023
PI
004
EXPLOSION
DOOR
PEEP DOOR
AI
028
O₂
AIC
027
TO FY-005 (REV B)
TI
024
SKIN
LP STEAM
(SNUFFING)
HV-221 NC
2"-LS-301
BS
005
BSLL
005
3"-P-105
TO PACKED-BED
REACTOR V-200
TT
040
TIC
030
TIAH
025
TE-025
TSHH
025
PI
005
DR
COMBUSTION AIR
FROM ATMOSPHERE
F-100
INTAKE SCREEN
AIR DUCT DN350 (TBC)
FE-005
FT
005
FV-200 FO
FIC
005
FY
005
AIR/FUEL RATIO (REV B)
FROM FI-001 & AIC-027
PT
030
PIAL
030
PSLL-030
(SIS-100)
FUEL OIL FROM
FUEL SYSTEM
1"-FO-201
V-121
PI
019
FE-001
FI
001
TO FY-005
XV-301
S
S
XV-303
BLEED TO SAFE LOC.
XV-302
S
FV-300 FC
PT
020
PIAL
020
PSLL-020
(SIS-100)
V-122
BURNER GUN
LEGEND
PROCESS LINE
UTILITY LINE
INSTRUMENT SIGNAL
MANUAL VALVE (GATE)
CONTROL VALVE, FO / FC = FAIL OPEN / CLOSED
S
SIS SHUT-OFF VALVE, SOLENOID
CHECK VALVE
FLOW ELEMENT (ORIFICE)
RELIEF VALVE (PSV)
PI
001
FIELD-MOUNTED INSTRUMENT
FIC
003
DCS FUNCTION (OPERATOR CONSOLE)
TSHH
025
SIS-100 / BMS FUNCTION
SERVICE CODES: P PROCESS HYDROCARBON · FO FUEL OIL
HF HEATING FLUID · LS LP STEAM · DR DRAIN
LINE NO. = SIZE - SERVICE - NUMBER
INTERLOCK SCHEDULE · SIS-100 / BMS
TRIP
CAUSE
SETTING
DELAY
FSLL-008
LOW FEED FLOW
< 3.4 L/s
5 s
TSHH-025
HIGH OUTLET TEMP.
> 375 °C
5 s
PSLL-020
LOW FUEL P AT GUN*
< 40 kPa
3 s
PSLL-030
LOSS OF WINDBOX DRAFT*
< 0.5 mmH₂O
3 s
BSLL-005
FLAME FAILURE
NO FLAME
2 s
HS-001
ESD PUSHBUTTON
MANUAL
0 s
* ARMED WHEN FIRING.
ANY TRIP: CLOSE XV-301 & XV-302, OPEN XV-303 BLEED,
CLOSE FV-300, OPEN FV-200 & HV-400 (POST-PURGE).
RESET ONLY FROM BMS AFTER 300 s PURGE; LIGHT-OFF
AT LOW FIRE (TIC-030 MAN 10-20 %), 10 s TRIAL.
GENERAL NOTES:
1. DESIGN BASIS: NATURAL DRAFT FIRED HEATER VER 1 OTS MODEL, DESIGN CASE. PRESSURES kPa g, DRAFT mmH₂O.
FEED 6.8 L/s = 19 584 kg/h (0.80 kg/L): 40 → 180 (E-100) → 233 (CROSSOVER) → 350 °C; PUMP DISCH. ≈ 1030, OUTLET ≈ 545.
FUEL 243 kg/h, LHV 42 MJ/kg: FIRED 2.84 MW, ABSORBED 2.31 MW (81.5 %). AIR 3 892 kg/h (11 % EXCESS).
FLUE GAS 4 380 kg/h AT 400 °C (INCL. ≈ 245 kg/h TRAMP AIR). DRAFT: ARCH -2.5, FLOOR -6.0, WINDBOX 5.25.
2. LINE SIZES PRELIMINARY FROM VELOCITY (LIQUID 1.5-2.5 m/s, AIR DUCT 10 m/s) - TBC BY HYDRAULIC CALCULATION.
3. PRESSURE INSTRUMENTS C/W ROOT AND TEST VALVES (TYP., NOT SHOWN). PUMP CASING VENTS/DRAINS TYP., NOT SHOWN.
4. XV-301 / XV-302 / XV-303 FORM A DOUBLE BLOCK AND BLEED, OPERATED BY SIS-100 (BMS); SIGNALS NOT SHOWN.
5. FV-010 FAILS OPEN SO THE COIL KEEPS FLOW ON AIR OR SIGNAL FAILURE; FV-300 FAILS CLOSED; FV-200 & HV-400 FAIL OPEN.
6. RADIANT AND CONVECTION COILS SHOWN SCHEMATICALLY; TUBE COUNT AND PASSES PER DESIGN TAB (SINGLE PASS).
7. FT-008 SERVES FIC-003, FIAL-008 AND FSLL-008 (HAZOP GAP: ADD FT-008B FOR THE TRIP - HOLD).
NOTES (CONT.):
8. TIC-030 MOVES FUEL ONLY. REV A: FIC-005 ON OWN SET POINT. REV B OPTION: FY-005 AIR/FUEL RATIO ON FI-001 + AIC-027 O₂ TRIM.
9. PSV-101 PROTECTS E-100 FEED SIDE; SET 1700 kPa g, F ORIFICE, GOVERNED BY FIRE (RELIEF LOAD BASIS NDFH-V1-PE-RLB-001).
10. PI-019 = FUEL HEADER (≈ 1940 kPa g). PT-020 = GUN PRESSURE (≈ 600 kPa g), DOWNSTREAM OF FV-300.
11. BS-005 UV FLAME SCANNER ON THE BURNER; LIGHT-OFF AND PURGE PER BMS SEQUENCE (LEGEND PANEL).
12. HV-221 SNUFFING STEAM, NORMALLY CLOSED; OPEN ONLY FOR A FIREBOX FIRE. EXPLOSION DOOR ON RADIANT WALL.
13. V-108 HIGH-POINT VENT AT COIL INLET (NC); V-109 E-100 CHANNEL DRAIN (LC); V-110 PSV-101 INLET (CSO). REV E: HAND VALVES TAGGED FOR THE 3-D PLANT.
14. ALARM SET POINTS: SEE WORKBOOK (ALARM TABLE); TRIP SET POINTS: INTERLOCK SCHEDULE.
REV
DESCRIPTION
DATE
B
RATIO FY-005 + O₂ TRIM AIC-027 (OPTION)
--
C
OTS SCREEN DRAWING (CURRENT, USED IN DECKS)
--
D
ALTERNATIVE VERSION, EPC STANDARD
29-SEP-26
E
HAND VALVES V-108 TO V-110, V-401, V-402 TAGGED
25-OCT-26
NATURAL DRAFT FIRED HEATER VER 1 · OTS
P&ID — H-100 · ALTERNATIVE VERSION
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 25-OCT-26
DWG NO.
NDFH-V1-PID-001
REV
E
SCALE
N.T.S.
SHEET
1 OF 1