## Slide 1
DRY AIR FROM
DRYING TOWER
K-101
MAIN AIR BLOWER
DN1800-PA-101
FI
100
FSLL
100
I-1
PI
101
FV-101
FO
FIC
101
FFC
101
DN1800-PA-103
FV-102
FO
FIC
102
DN700-PA-102
F-101
SULFUR
FURNACE
FUEL GAS
(START-UP)
H-101 PREHEAT
BURNER PKG
HIC
109
BMS / FLAME SAFEGUARD
BY VENDOR (NOTE 6)
TI
106
TV-201
FC
DN1200-SG-104
TI
107
BFW
SAT. STEAM
TO SH-201
FI
108
B-101
WASTE HEAT BOILER (FIRE-TUBE)
STEAM SIDE: NOTE 7
DN2600-SG-103
DN2800-PG-201
AIC
104
AI
105
SO2
O2
HV-112 (LC)
DN1200-PG-212 START-UP HOT-GAS LINE (NOTE 5)
TO BED 4 INLET
(START-UP) PID-002
BED 1
BED 2
BED 3
BEDS 4 & 5
SO3-PID-002
R-201
SO2 CONVERTER, 5 BEDS (3+2 DA)
BEDS 1-3 V2O5/K2SO4, BEDS 4-5 Cs-V2O5
TIC
201
TI
202
TI
212
TI
222
TSHH
203
I-2
PDI
204
PDI
214
PDI
224
TI
203
SH-201
STEAM
SUPERHEATER
TV-231
FO
TIC
231
PV: TT-231
(NOTE 4)
SAT. STEAM
FROM B-101
HP STEAM
TO HEADER
E-201
HOT INTERPASS
EXCHANGER
TV-211
FO
DN2800-PG-203
TIC
211
DN2800-PG-204
TI
213
E-202
COLD INTERPASS
EXCHANGER
TV-221
FO
DN2800-PG-205
TIC
221
DN2900-PG-206
TI
223
TO E-203
SO3-PID-002
FROM IPA T-301
SO3-PID-002
DN2000-PG-301
TO BED 4 INLET
SO3-PID-002
DN2000-PG-302
MOLTEN SULFUR FROM
SULFUR PIT (~140 °C)
P-101A
P-101B
XV-103
SIS I-1..6
FV-103
FC
FIC
103
DN80-MS-105 (JACKETED)
LEGEND
PROCESS LINE
UTILITY LINE
SIGNAL LINE
LINE JUMP (NO JOIN)
CONTROL VALVE FO/FC
SIS SHUT-OFF VALVE
MANUAL VALVE (LC)
ORIFICE ELEMENT
TI
DCS INSTRUMENT
TI
FIELD INSTRUMENT
TI
SIS FUNCTION
OFF-SHEET LINK
CATALYST BED
S&T EXCHANGER
CONTROL LOOP SCHEDULE
LOOP
MEASURES
MOVES
FAIL
SET / NOTE
FIC-103
SULFUR TO F-101
FV-103
FC
40.9 t/h (PRODUCTION)
FFC-101
AIR/SULFUR RATIO
FIC-101 SP
-
4.99 kNm3/t (14 % SO2)
FIC-101
COMBUSTION AIR
FV-101
FO
CAS, MIN 100 kNm3/h
AIC-104
SO2 INTO BED 1
FIC-102 SP
-
12.0 % SO2
FIC-102
DILUTION AIR
FV-102
FO
CAS FROM AIC-104
TIC-201
BED 1 INLET
TV-201 (B-101 BYP.)
FC
420 C
TIC-211
BED 2 INLET
TV-211 (E-201 BYP.)
FO
445 C
TIC-221
BED 3 INLET
TV-221 (E-202 BYP.)
FO
440 C
TIC-231
BED 4 INLET
TV-231 (SH-201 BYP.)
FO
425 C (NOTE 4)
TIC-241
BED 5 INLET
TV-241 (E-204 BYP.)
FO
428 C
TIC-251
GAS TO T-301
TV-251 (E-203 BYP.)
FO
190 C
HIC-109
-
H-101 FIRING
FC
START-UP ONLY
SIS INTERLOCKS (ACTION: SULFUR CUT)
I-
INITIATOR
SETTING
ACTION
1
FSLL-100 LOW TOTAL AIR
< 90 kNm3/h, 3 s
CLOSE XV-103
2
TSHH-203 BED 1 EXIT
> 660 C, 5 s
CLOSE XV-103
3
FSLL-301 IPA ACID FLOW
< 50 %, 10 s
CLOSE XV-103
4
FSLL-302 FAT ACID FLOW
< 50 %, 10 s
CLOSE XV-103
5
ASHH-306 STACK SO2
> 3000 ppm, 5 min *
CLOSE XV-103
6
HS-001 ESD PUSHBUTTON
MANUAL
XV-103 + STOP K-101, H-101
DESIGN POINT (OTS MODEL)
BED
IN C
OUT C
X %
PDI kPa
1
420
631
63.1
4.5
2
445
528
88.1
3.0
3
440
465
95.8
3.6
4
425
441
99.70
2.9
5
428
427
99.80
3.0
12.0 % SO2 / 9.0 % O2 INTO BED 1; STACK 286 ppm SO2;
PI-200 35 kPa g; K-101 DISCHARGE 60 kPa g.
GENERAL NOTES:
1. DESIGN BASIS: 1000 kt/y H2SO4 (100 %) AT 8000 h/y = 125 t/h; SULFUR 40.9 t/h BURNED IN 204.5 kNm3/h DRY AIR (14 % SO2), DILUTED TO 12.0 % SO2 / 9.0 % O2, 238.5 kNm3/h.
CONVERSION TARGETS 60/86/94/99.7/99.8 % PER PLANT SLIDE 5.2; BED TEMPERATURES FROM HEAT BALANCE (dH = -98.5 kJ/mol) - SEE DESIGN TABLE. GHSV 700 1/h, 340 m3 CATALYST (ASSUMED SPLIT 18/20/24/20/18 %).
2. DUCT AND LINE SIZES PRELIMINARY (VELOCITY 20-25 m/s GAS, 1.5 m/s SULFUR, 2.5 m/s ACID) - TBC BY PIPING. SERVICE CODES: PA PROCESS AIR, SG SO2 GAS, PG PROCESS GAS, MS MOLTEN SULFUR, SA SULFURIC ACID.
3. ALL CONTROL LOOPS IN DCS (SHARED DISPLAY). SIS FUNCTIONS I-1..I-6 IN A SEPARATE LOGIC SOLVER; XV-103 FAILS CLOSED. * ASHH-306 INHIBITED FOR 60 min AFTER SULFUR ADMISSION (START-UP).
4. BED 4 INLET IS SET BY THE HEAT LEFT IN THE BED-1 GAS FOR THE RETURN GAS: TIC-231 (TT-231 ON SO3-PID-002) BYPASSES SH-201; TIC-211 THEN HOLDS BED 2 VIA TV-211. LOOPS INTERACT - TUNE TIC-231 SLOW.
5. HV-112 START-UP HOT-GAS LINE LOCKED CLOSED IN OPERATION (ZSC-112 IS A PERMISSIVE FOR SULFUR ADMISSION); OPENED ONLY TO PREHEAT BEDS 4-5 BEFORE SULFUR IS ADMITTED.
6. H-101 PREHEAT BURNER: FLAME SAFEGUARD, FUEL SHUT-OFF VALVES AND IGNITER BY VENDOR; TRIPS ON LOW AIR (< 60 kNm3/h). START-UP ONLY.
7. B-101 STEAM SIDE (DRUM, LEVEL CONTROL, BLOWDOWN, PSV) AND SH-201 STEAM PIPING PER STEAM SYSTEM P&ID - OUTSIDE OTS SCOPE.
REV
DESCRIPTION
DATE
A
ISSUED FOR OTS DEVELOPMENT (REVIEW)
25-SEP-26
CHULA CHEM. ENG. - SO3 CONVERTER VER 1 (OTS)
P&ID - AIR, SULFUR FURNACE,
CONVERTER BEDS 1-3
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 25-SEP-26
DWG NO.
SO3-PID-001
REV
A
SCALE
N.T.S.
SHEET
1 OF 2

## Slide 2
BEDS 1-3
SO3-PID-001
BED 4
BED 5
R-201
SO2 CONVERTER
(LOWER PART, 2ND PASS)
TI
232
TI
242
PDI
234
PDI
244
FROM E-201 COLD SIDE
(SO3-PID-001)
DN2000-PG-302
START-UP LINE HV-112
(SO3-PID-001)
DN1200-PG-212
TT
231
TO TIC-231
(SO3-PID-001)
E-204
INTERBED
ECONOMIZER
(BFW: NOTE 4)
TV-241
FO
TI
233
TIC
241
TI
243
E-205
FINAL ECONOMIZER
BFW IN
BFW OUT
TI
252
DN2100-PG-304
MIST ELIM.
T-302
FINAL
ABSORBER
ST-301
STACK
DN2100-PG-305
AIT
306
AIT
307
ASHH
306
I-5
XI
308
CONVERSION
FROM BED 3
(PID-001)
E-203
IPA
ECONOMIZER
TV-251
FO
DN2400-PG-207
TIC
251
BFW IN
BFW OUT
MIST ELIM.
T-301
INTERPASS
ABSORBER
TO E-202 COLD SIDE
(SO3-PID-001)
DN2000-PG-301
TI
305
TK-301
P-301A
P-301B
ACID
COOLER +
DILUTION
(NOTE 2)
FI
301
FSLL
301
AI
303
TI
304
% H2SO4
I-3
HS-301B AUTO-START
TK-302
P-302A
P-302B
ACID
COOLER +
DILUTION
(NOTE 2)
FI
302
FSLL
302
I-4
PRODUCT ACID, DILUTION WATER AND ACID CROSS-FLOWS: ACID SYSTEM P&ID (NOTE 2)
LEGEND
PROCESS LINE
UTILITY LINE
SIGNAL LINE
LINE JUMP (NO JOIN)
CONTROL VALVE FO/FC
SIS SHUT-OFF VALVE
MANUAL VALVE (LC)
ORIFICE ELEMENT
TI
DCS INSTRUMENT
TI
FIELD INSTRUMENT
TI
SIS FUNCTION
OFF-SHEET LINK
CATALYST BED
S&T EXCHANGER
CONTROL LOOP SCHEDULE
LOOP
MEASURES
MOVES
FAIL
SET / NOTE
FIC-103
SULFUR TO F-101
FV-103
FC
40.9 t/h (PRODUCTION)
FFC-101
AIR/SULFUR RATIO
FIC-101 SP
-
4.99 kNm3/t (14 % SO2)
FIC-101
COMBUSTION AIR
FV-101
FO
CAS, MIN 100 kNm3/h
AIC-104
SO2 INTO BED 1
FIC-102 SP
-
12.0 % SO2
FIC-102
DILUTION AIR
FV-102
FO
CAS FROM AIC-104
TIC-201
BED 1 INLET
TV-201 (B-101 BYP.)
FC
420 C
TIC-211
BED 2 INLET
TV-211 (E-201 BYP.)
FO
445 C
TIC-221
BED 3 INLET
TV-221 (E-202 BYP.)
FO
440 C
TIC-231
BED 4 INLET
TV-231 (SH-201 BYP.)
FO
425 C (NOTE 4)
TIC-241
BED 5 INLET
TV-241 (E-204 BYP.)
FO
428 C
TIC-251
GAS TO T-301
TV-251 (E-203 BYP.)
FO
190 C
HIC-109
-
H-101 FIRING
FC
START-UP ONLY
SIS INTERLOCKS (ACTION: SULFUR CUT)
I-
INITIATOR
SETTING
ACTION
1
FSLL-100 LOW TOTAL AIR
< 90 kNm3/h, 3 s
CLOSE XV-103
2
TSHH-203 BED 1 EXIT
> 660 C, 5 s
CLOSE XV-103
3
FSLL-301 IPA ACID FLOW
< 50 %, 10 s
CLOSE XV-103
4
FSLL-302 FAT ACID FLOW
< 50 %, 10 s
CLOSE XV-103
5
ASHH-306 STACK SO2
> 3000 ppm, 5 min *
CLOSE XV-103
6
HS-001 ESD PUSHBUTTON
MANUAL
XV-103 + STOP K-101, H-101
DESIGN POINT (OTS MODEL)
BED
IN C
OUT C
X %
PDI kPa
1
420
631
63.1
4.5
2
445
528
88.1
3.0
3
440
465
95.8
3.6
4
425
441
99.70
2.9
5
428
427
99.80
3.0
12.0 % SO2 / 9.0 % O2 INTO BED 1; STACK 286 ppm SO2;
PI-200 35 kPa g; K-101 DISCHARGE 60 kPa g.
GENERAL NOTES:
1. SEE SO3-PID-001 NOTES 1-3 FOR DESIGN BASIS, LINE SIZING AND SIS PHILOSOPHY. RETURN GAS FROM T-301 IS REHEATED IN E-202 THEN E-201 (SO3-PID-001) BEFORE BED 4.
2. T-301 / T-302 ACID CIRCULATION: PUMP TANKS, ACID COOLERS, DILUTION WATER AND PRODUCT ACID CONTROLS ARE ON THE ACID SYSTEM P&ID - SHOWN HERE AS PACKAGE LIMITS.
3. FSLL-301 ALSO AUTO-STARTS SPARE P-301B (HS-301B ARMED); P-302B IS STARTED MANUALLY. LOSS OF ACID CIRCULATION > 10 s TRIPS SULFUR (I-3, I-4).
4. E-203/E-204/E-205 ECONOMIZERS: BFW SIDE ON STEAM SYSTEM P&ID. E-204 BYPASS (TV-241) SETS BED 5 INLET; E-203 BYPASS (TV-251) KEEPS GAS TO T-301 ABOVE THE ACID DEW POINT.
5. AIT-306 / AIT-307 STACK ANALYZERS: SO2 (ppmv, DRY) AND SO3/H2SO4 MIST (mg/Nm3). XI-308 OVERALL CONVERSION CALCULATED IN DCS FROM AI-104, FI-100 AND AIT-306.
6. BED TEMPERATURES AND CONVERSIONS ARE THE OTS DESIGN POINT (SO3 CONVERTER VER 1); PLANT VALUES TBC.
REV
DESCRIPTION
DATE
A
ISSUED FOR OTS DEVELOPMENT (REVIEW)
25-SEP-26
CHULA CHEM. ENG. - SO3 CONVERTER VER 1 (OTS)
P&ID - INTERPASS ABSORPTION,
BEDS 4-5, FINAL ABSORPTION
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 25-SEP-26
DWG NO.
SO3-PID-002
REV
A
SCALE
N.T.S.
SHEET
2 OF 2