## Slide 1
P-400
Feed Supply Pump (upstream)
E-400
Feed Preheater (hot oil)
D-400
Flash Drum
FLASH DRUM VER 1 - OPERATOR TRAINING SIMULATOR
PROCESS FLOW DIAGRAM
D-400 FLASH DRUM UNIT - FEED PREHEAT, LET-DOWN AND FLASH
DRAWING No.
FD-400-PFD-001
REV.
0
SIZE
A4
SHEET
1 OF 1
DRAWN
Apinan Soottitantawat
CHECKED
SCALE
NTS
DATE
2026-09-29
LEGEND
Mass Flow (kg/h)
Temperature (°C)
Pressure (kPa g)
Process Line
Utility Line
Control Valve
Process Input / Output
Stream Number
Line Crossing
Centrifugal Pump
Heat Exchanger
Separator
DESIGN BASIS
Feed 16 m3/h, 35 wt% n-butane / 65 wt% n-hexane
D-400 1.6 m ID x 4.8 m T/T, 102.7 kPa g, 49.2 °C
E-400 duty about 420 kW, hot oil 180 -> 120 °C
NOTES
1. Flows in kg/h; temperatures in °C; pressures in kPa g. Stream data: D-400 design case.
2. P-400 and the hot-oil system are outside the unit; shown as supplies.
3. PSV-400 set 450 kPa g (MAWP). N2 blanket PCV-430 holds 30 kPa g.
1
2
10208
10
600
3
74
550
4
1714
49.2
102.7
5
8491
49.2
10980
180
120
P-400
E-400
hot oil
D-400
Feed from Tankage
35 wt% n-butane
Hot Oil Supply
Hot Oil Return
Fuel-Gas Header
76.8 wt% n-butane
Flare
Nitrogen
To Downstream Unit
26.6 wt% n-butane
Bypass
Relief (PSV-400)
FCV-400
TCV-401 (3-way)
PCV-420
LCV-400
PCV-430
FT-400