## Slide 1
FROM TANK FARM
DN100-GO-200
FI
199
HIC-199 (TANK FARM)
VENT (TBC)
T200
FEED STORAGE TANK
CONE ROOF, ATM
Ø12.0 × 10.0 m (TBC)
GAS OIL, 60 °C
LI
200
LSLL
200
I-1
DR
V200
S-200
DN150-GO-201
PI
209
V202
PI
210
NRV-210
V201
DN100-GO-202
VENT
M
P-200A
FEED PUMP A (DUTY)
14 L/s @ 33.5 m · 3600 rpm · 10 kW
II
210
TI
212
TSHH-212 (I-2)
V206
PI
220
NRV-220
V205
DN100-GO-203
VENT
M
P-200B
FEED PUMP B (SPARE)
14 L/s @ 33.5 m · 3600 rpm · 10 kW
II
220
TI
222
TSHH-222 (I-2)
COMMON
DISCHARGE
DN100-GO-204
LOW-POINT DR
TO OWS
FE-100
FRC
100
REMOTE SP (FCC)
FC
V100
DN100-GO-205
E-100 FEED PREHEATER
SHELL STEAM · TUBES FEED
2.3 MW, 60 → 150 °C (TBC)
MP STEAM 11 bar a
TV-110
FC
FI
112
PI
111
ST
TO CONDENSATE RETURN
TIC
110
DN100-GO-206
D-150
CAT-CRACKER FEED DRUM, 30 m³
LI
150
LSHH
150
I-4
PSV-150
SET HOLD
TO FLARE
TO CAT-CRACKER CHARGE
PUMPS (BY OTHERS)
FI
151
DN100-GO-207
LALL-150 (FCC SIDE)
LEGEND
HAND GATE VALVE (V200, V201, V202, V205, V206)
SWING CHECK VALVE, FLOW → (NRV-210/220)
CONTROL VALVE, DIAPHRAGM, FC = FAIL CLOSED
STRAINER
RESTRICTION ORIFICE / FLOW ELEMENT
M
ELECTRIC MOTOR DRIVER (PUMP: CIRCLE + BASE)
PI
LOCAL INSTRUMENT (NO DCS SIGNAL)
FRC
DCS INSTRUMENT (SHARED DISPLAY)
LSLL
SIS / TRIP FUNCTION
INSTRUMENT SIGNAL
PROCESS LINE, FLOW DIRECTION
UTILITY / DRAIN / VENT LINE
CONNECTION (TEE)
LINE NUMBER: DNxxx-SVC-nnn
GO = GAS-OIL FEED · SIZES INDICATIVE (TBC)
MP STEAM / CONDENSATE: UTILITY LINES
PUMP DATA (CASE)
P-200A
P-200B
SPEED, rpm
3600
3600
MOTOR, kW
10
10
SHUT-OFF HEAD, m
45.0
46.5
RATED
14 L/s
14 L/s
ΔH @ 14 L/s, m
32.0
33.5
GENERAL NOTES
1. DESIGN BASIS: 14 L/s TO THE CAT CRACKER; P-200A/B IDENTICAL, 3600 rpm, 10 kW (UPRATED FROM 1800 rpm).
SHUT-OFF HEAD A 45.0 m, B 46.5 m. B RUNNING: PI-220 34 m, IDLE PI-210 0.5 m, V100 OUTPUT ≈ 80 %.
2. FLUID GAS OIL, 870 kg/m³, 60 °C, Pv 0.3 kPa: ASSUMED FOR THE OTS (TBC). HEADS ON THIS SHEET ARE IN METRES OF LIQUID (1 m = 8.5 kPa).
3. T200 SIZE, SUCTION LOSSES (3.5 m AT 14 L/s), DELIVERY STATIC + BACK PRESSURE (24 m), E-100 AND D-150 DATA: ASSUMED (TBC).
4. PI-209, PI-210, PI-220 ARE LOCAL GAUGES ONLY. PI-210/220 SIT BETWEEN PUMP AND CHECK VALVE: THEY READ THE CASING, NOT THE HEADER.
5. PRESSURE INSTRUMENTS C/W ROOT & TEST VALVES (TYP., NOT SHOWN). PUMP CASING DRAINS TO CLOSED DRAIN (TYP., NOT SHOWN).
6. V100 AND TV-110 FAIL CLOSED. NO BLOCK / BYPASS AROUND V100 ON THE AS-FOUND DRAWING (TBC).
7. FRC-100 SET POINT IS REMOTE FROM THE CAT CRACKER (14 L/s). TIC-110 NORMALLY IN MAN.
8. LINE SIZES INDICATIVE ONLY (TBC). PSV-150 SET PRESSURE AND FLARE TIE-IN: HOLD.
9. DESIGN POINT (A RUNNING): PI-209 0.5 m, PI-210 32.4 m, FRC-100 14 L/s, V100 84 %, II-210 13.2 A, TI-110 150 °C.
INTERLOCKS AND OPERATING NOTES
I-1 LSLL-200 (10 %, 5 s) TRIPS P-200A AND P-200B (LATCHED). LSL-200 (15 %) BLOCKS PUMP STARTS.
I-2 TSHH-212 / TSHH-222 (110 °C, 5 s, ON THE TI-212 / TI-222 ELEMENT) TRIP THEIR OWN MOTOR.
I-3 MOTOR OVERLOAD 49-210 / 49-220 AT THE MCC (21.7 A, 10 s) TRIP THEIR OWN MOTOR.
I-4 LSHH-150 (95 %) FORCES V100 CLOSED (LATCHED UNTIL RESET BELOW 90 %). ESD STOPS BOTH PUMPS, CLOSES V100 AND TV-110.
A. START-UP: SUCTION OPEN, CASING VENTED FULL, DISCHARGE CLOSED; CONFIRM SHUT-OFF HEAD ON THE LOCAL GAUGE; OPEN DISCHARGE WITHIN 2 min.
B. REV A (AS FOUND): SPARE P-200B LINED UP WITH ITS SUCTION V206 AND DISCHARGE V205 OPEN.
C. PROPOSED UPGRADES (REV C, SEE SIS TAB): PIT-210/220 TO DCS WITH PAH ON THE IDLE CASING; MOV DISCHARGE
VALVES INTERLOCKED WITH THE MOTORS. NOT SHOWN ON THIS SHEET.
D. THE SIMULATOR SCREEN P&ID IS THE REFERENCE FOR THE DCS, DECKS AND EXERCISES; THIS SHEET IS AN ALTERNATIVE VERSION.
REV
DESCRIPTION
DATE
A
AS FOUND · ISSUED FOR OTS
25-SEP-26
B
ALTERNATIVE VERSION · EPC STANDARD
09-OCT-26
CHEM ENG CHULALONGKORN UNIVERSITY · OTS
P&ID P-200A/B · ALTERNATIVE VERSION
DRAWN:
APINAN SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 09-OCT-26
DWG NO.
PPS-PID-001
REV
B
SCALE
N.T.S.
SHEET
1 OF 1