## Slide 1
T200
Feed Storage Tank (cone roof)
S-200
Suction Strainer
P-200A
Feed Pump A (running)
P-200B
Feed Pump B (spare)
E-100
Feed Preheater (steam)
D-150
Cat-Cracker Feed Drum
PARALLEL PUMP STATION VER 1 · OPERATOR TRAINING SIMULATOR
PROCESS FLOW DIAGRAM
PARALLEL PUMP STATION — CAT-CRACKER FEED, T200 TO D-150
DRAWING No.
PPS-PFD-100
REV.
0
SIZE
A4
SHEET
1 OF 1
DRAWN
Apinan Soottitantawat
CHECKED
SCALE
NTS
DATE
2026-10-08
LEGEND
Liquid Flow (L/s)
Mass Flow (t/h)
Temperature (°C)
Pressure (bar g)
Process Line
Utility Line
Block Valve
Control Valve
Process Input / Output
Stream Number
Line Crossing
Storage Tank
Filter
Centrifugal Pump
Heat Exchanger
Vessel / Drum
NOTES
1. Flags: OTS design state — P-200A running, P-200B spare lined up (idle), FRC-100 AUTO 14 L/s, TIC-110 MAN 50 %.
2. Gas oil 870 kg/m3, 60 °C in T200. Pressures in bar g from the model heads (m of liquid); steam in bar g in the E-100 shell.
3. Suction and discharge block valves, check valves NRV-210/220, local gauges, drains, vents and trips: see P&ID PPS-PID-001.
4. Sizes: T200 Ø12 x 10 m, D-150 30 m3 (model); other symbols indicative.
1
14.0
60.0
2
3
14.0
0.04
4
5
6
14.0
60.1
2.77
7
8
14.0
2.73
9
14.0
150.1
10
14.0
150.1
4.03
4.96
T200
S-200
P-200A
P-200B
E-100
steam
D-150
Gas Oil from Tank Farm
Steam 11 bar a
Condensate
Charge to Cat Cracker
FRC
HIC
TIC