## Slide 1
BED 1 · 25.0 t
BED 2 · 41.7 t
BED 3 · 58.3 t
BED 4 · 83.3 t
INLET DISTRIBUTOR
OUTLET COLLECTOR
R-201
METHANOL QUENCH CONVERTER
4 ADIABATIC BEDS, Cu/ZnO/Al2O3 184 m3
FROM E-202 COLD SIDE (MEOH-PID-002)
CONVERTER FEED ~97 C, 80 bar g
AIT
205
CO / CO2 /
CH4 (INLET)
DN750-PG-201
FI
212
FI
222
TV-221
FO
DN300-PG-222
TIC
221
FI
232
TV-231
FO
DN350-PG-232
TIC
231
FI
242
TV-241
FO
DN350-PG-242
TIC
241
QUENCH (COLD SHOT)
HEADER ~97 C
DN600-PG-213
TIC
211
E-204
START-UP
HEATER
HV-214
FC (HIC-214)
HP STEAM 40 bar g
COND.
TV-211
FO
E-201 COLD-SIDE
BYPASS
E-201
FEED/EFFLUENT
INTERCHANGER
(HOT)
TI
205
DN900-PG-251
EFFLUENT ~268 C
TO E-202 HOT SIDE
(MEOH-PID-002)
TI
251
AIT
208
CH3OH
(OUTLET)
TI
212-214
PDI
215
TI
222-224
PDI
225
TI
232-234
PDI
235
TI
242-244
PDI
245
TSHH
2xx
I-1 (NOTE 4)
LEGEND
PROCESS LINE
UTILITY LINE
SIGNAL LINE
LINE JUMP (NO JOIN)
CONTROL VALVE FO/FC
SIS SHUT-OFF VALVE
MANUAL VALVE
ORIFICE ELEMENT
TI
DCS INSTRUMENT
TI
FIELD INSTRUMENT
TI
SIS FUNCTION
OFF-SHEET LINK
CATALYST BED
QUENCH DISTRIBUTOR
CONTROL LOOP SCHEDULE
LOOP
MEASURES
MOVES
FAIL
SET / NOTE
FIC-201
CONVERTER FEED
C-201 SPEED (SC)
-
1928 kNm3/h
FIC-202
MAKE-UP SYNGAS
FV-202
FC
366 kNm3/h (RATE)
PIC-203
LOOP PRESS. V-201
PV-203 PURGE
FC
75.0 bar g
LIC-204
V-201 LEVEL
LV-204
FC
50 %
TIC-211
BED 1 INLET
TV-211 (E-201 BYP.)
FO
220 C
TIC-221
BED 2 INLET
TV-221 QUENCH 2
FO
225 C
TIC-231
BED 3 INLET
TV-231 QUENCH 3
FO
230 C
TIC-241
BED 4 INLET
TV-241 QUENCH 4
FO
235 C
HIC-214
-
E-204 STEAM
FC
START-UP ONLY
SIS INTERLOCKS (ACTION: MAKE-UP CUT)
I-
INITIATOR
SETTING
ACTION
1
TSHH-2xx ANY BED TC
> 300 C, 5 s
XV-202 + E-204 OFF
2
FSLL-201 CIRCULATION
< 45 %, 5 s *
XV-202 + E-204 OFF
3
LSHH-204 V-201 LEVEL
> 90 %, 5 s
XV-202 + STOP C-201
4
PSHH-203 LOOP PRESS.
> 85 bar g, 5 s
XV-202 + E-204 OFF
5
HS-200 ESD PUSHBUTTON
MANUAL
XV-202 + C-201 + E-204
DESIGN POINT (OTS MODEL)
BED
IN C
OUT C
MeOH %
CAT. t
1
220
260
2.1
25.0
2
225
277
3.6
41.7
3
230
270
4.4
58.3
4
235
268
4.8
83.3
CONVERTER 80 bar g IN; V-201 75 bar g / 40 C; FEED 1928 kNm3/h;
MAKE-UP 366 kNm3/h; PURGE 105 kNm3/h; MeOH 112.5 t/h; Q(RXN) 85 MW.
* ARMED ONLY WITH XV-202 OPEN.
GENERAL NOTES:
1. DESIGN BASIS (REFERENCE CARD): 900 kt/y CH3OH AT 8000 h/y = 112.5 t/h; QUENCH CONVERTER, FIXED BED, GAS PHASE, 220-280 C, 50-100 bar, Cu/ZnO/Al2O3, GHSV 8000-12000 1/h. OTS DESIGN: 80 bar g INLET,
184 m3 CATALYST (12/20/28/40 %, 1150 kg/m3), GHSV 10 500 1/h, FEED 1928 kNm3/h; BED TEMPERATURES AND FLOWS FROM THE OTS HEAT AND MASS BALANCE (KINETICS VANDEN BUSSCHE & FROMENT 1996, ASSUMED) - PLANT VALUES TBC.
2. LINE SIZES PRELIMINARY (GAS 20 m/s, LIQUID 2 m/s) - TBC BY PIPING. SERVICE CODES: PG PROCESS GAS, SG SYNGAS, PU PURGE, CM CRUDE METHANOL, HS HP STEAM, SC CONDENSATE, CW COOLING WATER, FL FLARE.
3. COLD SHOTS ENTER THROUGH LOZENGE DISTRIBUTORS ABOVE BEDS 2-4; TIC-221/231/241 MEASURE JUST BELOW EACH DISTRIBUTOR. QUENCH VALVES AND TV-211 FAIL OPEN (CONVERTER GOES COLDER ON AIR FAILURE).
4. TSHH-2xx: ANY OF THE BED MULTIPOINT THERMOCOUPLES TE-212...244 ABOVE 300 C FOR 5 s (VOTING TBC) - I-1 CLOSES XV-202 (MAKE-UP) AND FORCES HV-214 SHUT; C-201 KEEPS CIRCULATING TO COOL THE BEDS.
5. E-204 START-UP HEATER (HP STEAM, MAX 30 MW) IN SERVICE ONLY TO HEAT THE CATALYST TO ~210 C BEFORE MAKE-UP GAS IS ADMITTED; HV-214 BLOCKED IN DURING NORMAL OPERATION.
6. PDI-215...245 TAPS ABOVE AND BELOW EACH BED (NOT SHOWN). CONVERTER RELIEF IS PROVIDED BY PSV-201 ON V-201 (MEOH-PID-002); CATALYST DUMP NOZZLES, MANWAYS, VENTS AND DRAINS NOT SHOWN.
7. TIC-211 SETS THE BED 1 INLET BY BYPASSING PART OF THE BED-1 FEED AROUND THE COLD SIDE OF E-201 (FEED/EFFLUENT POSITIVE FEEDBACK - TUNE SLOW, CHECK AFTER ANY RATE CHANGE).
REV
DESCRIPTION
DATE
A
ISSUED FOR OTS DEVELOPMENT (REVIEW)
25-SEP-26
CHULA CHEM. ENG. - METHANOL CONVERTER VER 1 (OTS)
P&ID - METHANOL CONVERTER R-201,
INTERCHANGER E-201, E-204
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 25-SEP-26
DWG NO.
MEOH-PID-001
REV
A
SCALE
N.T.S.
SHEET
1 OF 2