## Slide 1
E-101 BFW STEAM HEATER
SHELL: FLASH STEAM · TUBES: BFW, 1 PASS, 100 TUBES
TK-101
BFW TANK
18 °C
BFW MAKE-UP
(NOTE 11)
8"-BW-100
V-106
P-101A
MOTOR
NRV-101
V-108
V-107
P-101B
MOTOR
NRV-102
V-109
PI
106
3"-BW-102
FV-101B (NOTE 6)
6"-BW-101
FE-101
FT
101
FSLL
101
V-110
V-111
FV-101A FO
FIC
101
V-112
BYPASS
TI
103
6"-BW-101
6"-BW-103
TO DEAERATOR
(BOILER HOUSE)
TT
101
TIC
101
TT
108
TIAH
108
TSHH
108
PDT
109
PDI
109
FLASH STEAM HEADER
200 kPa g
12"-LS-101
14"-LS-102
PI
105
XV-100
S
FE-104
FT
104
FIC
104
V-113
V-114
FV-104 FC
V-115 BYPASS
RSP
PT
100
PI
100
PSHH
100
NOTE 7
TI
100
PSV-100
SET TBC (NOTE 9)
TO SAFE LOC.
VB-101
V-104
RO-101 (REV B)
1"-VT-101
AAV-101 (REV C)
TI
102
VENT TO SAFE LOC.
TAL (REV C)
3"-SC-101
V-101
Y-101
T
ST-101
V-102
4"-SC-102
COND. RETURN 30 kPa g
V-103 TRAP BYPASS (NC)
V-105 DR
LEGEND
PROCESS LINE
UTILITY LINE (STEAM, VENT, RELIEF)
INSTRUMENT SIGNAL
MANUAL VALVE (GATE)
CONTROL VALVE, FO / FC = FAIL OPEN / CLOSED
S
SIS SHUT-OFF VALVE, SOLENOID, FAIL CLOSED
CHECK VALVE
FLOW ELEMENT (ORIFICE)
T
STEAM TRAP
RELIEF VALVE (PSV)
TT
101
FIELD-MOUNTED INSTRUMENT
FIC
101
DCS FUNCTION (OPERATOR CONSOLE)
TSHH
108
SIS FUNCTION
SERVICE CODES: BW BOILER FEED WATER · LS FLASH STEAM
SC STEAM CONDENSATE · VT VENT · DR DRAIN
LINE NO. = SIZE - SERVICE - NUMBER (SIZES TBC, NOTE 2)
INTERLOCK SCHEDULE · SIS I-100
TAG
CAUSE
SETTING
DELAY
FSLL-101
LOW BFW FLOW *
< 30 m³/h
5 s
TSHH-108
HIGH BFW OUTLET TEMP.
> 95 °C
5 s
PSHH-100
HIGH SHELL PRESSURE
> 250 kPa g
3 s
HS-ESD
ESD PUSHBUTTON (DCS)
MANUAL
0 s
PSV-100
E-101 SHELL OVERPRESSURE
TBC
MECH.
EFFECTS (I-100):
ANY TRIP: CLOSE XV-100 (STEAM SHUT-OFF);
FIC-104 TO MAN 0 %; TIC-101 TO MAN.
* ARMED ONLY WHEN THE SIS IS IN RUN (STEAM ON).
RESET BLOCKED WHILE TSHH-108 OR PSHH-100 IS ACTIVE.
OPEN XV-100 NEEDS: SIS RESET (IDLE), FIC-101 ≥ 50 m³/h,
FIC-104 IN MAN ≤ 10 %, V-101 AND V-102 OPEN.
GENERAL NOTES:
1. DESIGN BASIS: BFW STEAM HEATER VER 1 OTS MODEL, DESIGN CASE. PRESSURES kPa g.
BFW 100 m³/h (27.7 kg/s) 18 → 70 °C: DUTY 6.04 MW. FLASH STEAM 9 935 kg/h FROM THE 200 kPa g HEADER (PI-105 195),
SHELL 105 kPa g / 121.3 °C (λ 2 189 kJ/kg). P-101 DISCHARGE PI-106 662; TUBE-SIDE ΔP PDI-109 60 kPa.
CONDENSATE TO THE 30 kPa g RETURN; HOTWELL LEVEL ≈ 5 % OF SHELL DIAMETER (TUBES START AT 12 %).
2. LINE SIZES FROM VELOCITY (BFW 6 in 1.5 m/s; STEAM 12 in 24 m/s, 14 in 28 m/s; CONDENSATE 3 in 0.6 m/s) - TBC.
3. PRESSURE INSTRUMENTS C/W ROOT AND TEST VALVES; PUMP CASING AND CHANNEL VENTS/DRAINS; TYP., NOT SHOWN.
4. XV-100 FAILS CLOSED, OPERATED BY SIS I-100 (SIGNALS NOT SHOWN). FV-104 FC, FV-101A FO.
5. TIC-101 SETS THE FIC-104 STEAM-FLOW SET POINT (CASCADE, RSP).
6. FV-101B MINIMUM-FLOW RECYCLE OPENS AS 100 − FIC-101 OUT (SPLIT); FAIL POSITION NOT IN THE OTS MODEL - TBC.
7. PSHH-100 SHARES PT-100 WITH PI-100, FSLL-101 SHARES FT-101 WITH FIC-101: OWN TRANSMITTERS RECOMMENDED - HOLD.
TSHH-108 / TIAH-108 HAVE THEIR OWN TT-108, INDEPENDENT OF TT-101.
NOTES (CONT.):
8. NON-CONDENSABLES COLLECT AT THE SHELL END FURTHEST FROM THE STEAM INLET; V-104 VENTS THERE.
REV B: RO-101 CONTINUOUS VENT. REV C: AAV-101 AUTOMATIC AIR VENT WITH TI-102 / TAL-102.
9. PSV-100 SET PRESSURE AND SHELL / TUBE DESIGN PRESSURES ARE NOT IN THE OTS DATA (350 / 1 100 kPa g ASSUMED
IN THE DESIGN TAB) - TBC. TUBE RUPTURE IS A RELIEF CASE BEYOND PSV-100: RUPTURE DISC RD-100 RECOMMENDED, HOLD.
10. VB-101 VACUUM BREAKER ADMITS AIR WHEN THE SHELL GOES BELOW ATMOSPHERIC (CONDENSATE HOLD-UP, WATER HAMMER).
11. TK-101 MAKE-UP AND LEVEL CONTROL OUTSIDE THE OTS SCOPE. HOTWELL LEVEL INDICATION NOT FITTED - RECOMMENDED, HOLD.
12. V-103 TRAP BYPASS NORMALLY CLOSED; OPEN IT PASSES LIVE STEAM TO THE RETURN HEADER.
13. ALARM SET POINTS: SEE WORKBOOK (ALARM TABLE); TRIP SET POINTS: INTERLOCK SCHEDULE.
14. V-106 TO V-115 AND NRV-101/102 ARE NUMBERED ON THIS SHEET; V-101 TO V-105 AS ON THE SCREEN DRAWING.
REV
DESCRIPTION
DATE
B
RO-101 CONTINUOUS VENT (OPTION)
--
C
AAV-101 + TI-102; OTS SCREEN DWG (USED IN DECKS)
--
D
ALTERNATIVE VERSION, EPC STANDARD
03-OCT-26
BFW STEAM HEATER VER 1 · OTS
P&ID — E-101 · ALTERNATIVE VERSION
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 03-OCT-26
DWG NO.
BFWH-V1-PID-001
REV
D
SCALE
N.T.S.
SHEET
1 OF 1