## Slide 1
TK-101
BFW Storage Tank
P-101 A/B
BFW Pumps
E-101
BFW Heater (steam in shell)
Y-101
Condensate Strainer
ST-101
Steam Trap
BFW STEAM HEATER VER 1 - OPERATOR TRAINING SIMULATOR
PROCESS FLOW DIAGRAM
BFW STEAM HEATER E-101 - FLASH-STEAM BFW HEATING
DRAWING No.
BFW-PFD-100
REV.
0
SIZE
A4
SHEET
1 OF 1
DRAWN
Apinan Soottitantawat
CHECKED
SCALE
NTS
DATE
2026-09-29
LEGEND
Mass Flow (1000 kg/h)
Temperature (°C)
Pressure (kPa g)
Process Line
Utility Line
Block Valve
Control Valve
Process Input / Output
Stream Number
Line Crossing
Storage Tank
Centrifugal Pump
Heat Exchanger
Filter
Vessel / Drum
NOTES
1. Flows in 1000 kg/h; temperatures in °C; pressures in kPa g. Design point of the simulator model.
2. Stream 8: vent V-104, trap bypass V-103 and shell drain V-105, all closed at design (no flags).
3. XV-100 is the SIS steam shut-off (FSLL-101, TSHH-108, PSHH-100, ESD).
1
110.5
18
2
10.7
18
662
3
99.8
18
662
4
99.8
70
602
5
9.94
133
195
6
9.94
121
105
8
7
9.94
119
30
TK-101
P-101 A/B
E-101
lps
Y-101
ST-101
Flash Steam Header
BFW to Boiler House (Deaerator)
Vent to Safe Location
Condensate Return Header
Relief to Safe Location
Air (Atmosphere)
Drain to Sewer
XV-100 (SIS)
FT-104
FV-104 (FC)
PSV-100
VB-101
V-104
FV-101B
FV-101A (FO)
V-105
V-103 (bypass)