## Slide 1
TO FLARE KO DRUM
AND FLARE (PID-900)
DN500-FL-100 (SIZE HOLD) · STREAM 13
FI
109
FL-115
FL-116
PRODUCTION GAS FROM
HP SEPARATOR (PID-001)
200 MMSCFD · 30.3 barg · 35 °C
DN500-PG-101 · STREAM 1
XV-001
FC
XY
001
FI
001
PIC
102
PSHH
001
PV-102
FO
PSV-001
36 barg
ESDV-101
FC
FC
HV-101 (HIC-101)
DN50-PG-114
XY
101
MESH
V-101
INLET
SCRUBBER
DN500-PG-102
LIC
101
LSHH
101
FC
LV-101
TO CLOSED DRAIN (CD)
STREAM 14 · DN50-CD-110
MV-130
CD
MV-135
VENT
PIC
101
PSLL
101
TI
101
BDV-101
FO
RO 45 mm
FL-117
HV-102 (HIC-102)
FC
DN50-FL-118
K-100 EXPORT GAS COMPRESSOR (1 CASING · 2 SECTIONS · 1 SHAFT)
SECTION 1
r 2.0 · 4 IMP.
SECTION 2
r 2.0 · 4 IMP.
SECTION 1: 7.95 MW · Ep 0.685 · 105 °C OUT
SECTION 2: 8.30 MW · Ep 0.655 · 116 °C OUT
DESIGN 9 500 rpm · SETTLE-OUT ≈ 69 barg (NOTE 3)
DN400-PG-103
TI
104
TSHH
104
PI
104
VI
105
VSHH
105
FI
103
UIC
103
FO
UV-103
DN300-PG-104
LP RECYCLE
E-101
INTERCOOLER
FO
CMS
CMR
TV-106
CM-120
CM-121
DN350-PG-112
TIC
106
MESH
V-102
INTERSTAGE
SCRUBBER
DN350-PG-105
MV-134 VENT
LIC
107
LSHH
107
FC
LV-107
CD
STR. 10
DN50-CD-111
CD
MV-131
PI
107
FI
108
UIC
108
DN300-PG-106
DN300-PG-113
PI
109
TI
109
TSHH
109
VI
110
VSHH
110
FO
UV-108
DN250-PG-107
HP RECYCLE
E-102
AFTERCOOLER
FO
CMS
CMR
TV-111
CM-122
CM-123
EXPORT GAS
TO ONSHORE TERMINAL
(36-in PIPELINE)
120 barg · 45 °C
DN400-EG-108
STREAM 8
AI
115
PI
114
PI
900
ONSHORE
TELEMETRY
MV-133
CD
TIC
111
PI
112
PSHH
112
FO
BDV-112
RO 45 mm
FL-119
NRV
ESDV-113
FC
FI
114
GT-100
TWO-SHAFT GAS TURBINE
22 MW ISO · 19.9 MW AT 30 °C
DIRECT DRIVE 9 500 rpm
EXHAUST
AIR
TI
099
TI
100
SIC
100
SSHH
100
JI
100
FUEL GAS
(NOTE 6)
XV-100
FC
FC
FV-100
FI
100
DN100-FG-109
STREAM 9
LUBE-OIL CONSOLE
P-150A
P-150B
B = STANDBY,
AUTO-START
ON PI-150 LOW
LO TO
BEARINGS
MV-132
CASING DRAIN TO CD
PI
150
PSLL
150
TI
151
LINE LIST · PRELIMINARY SIZES (NOTE 2)
LINE NO.
FROM → TO
STR.
kg/s
v m/s
DN500-PG-101
HP SEPARATOR → V-101
1
61.75
10.7
DN500-PG-102
V-101 → SECTION 1
2
61.75
10.8
DN400-PG-103
SECTION 1 → E-101
3
61.75
10.2
DN350-PG-112
E-101 → V-102
4
61.75
10.6
DN350-PG-105
V-102 → SECTION 2
5
60.26
10.4
DN300-PG-106
SECTION 2 → E-102
6
60.26
8.8
DN300-PG-113
E-102 → EXPORT HEADER
7
60.26
6.8
DN400-EG-108
HEADER → PIPELINE
8
60.25
3.8
DN100-FG-109
V-102 OUT → GT-100
9
1.38
7.4
DN300-PG-104
UV-103 RECYCLE
11
38.4*
9.0*
DN250-PG-107
UV-108 RECYCLE
12
37.4*
6.0*
DN50-CD-111
LV-107 → CLOSED DRAIN
10
0.11
LIQ.
DN50-CD-110
LV-101 → CLOSED DRAIN
14
0.22
LIQ.
* AT THE SURGE LINE q = 0.62, DESIGN SPEED (FULL RECYCLE CASE)
LEGEND
CONTROL VALVE (DCS) · FC / FO = FAIL CLOSED / OPEN
ESDV / BDV / XV ON-OFF VALVE (SIS), FAIL AS MARKED
REMOTE HAND VALVE HV (HIC IN THE DCS)
MANUAL VALVE MV (DRAIN / VENT / ISOLATION)
CHECK VALVE (NRV)
PRESSURE SAFETY VALVE (PSV) TO FLARE
FLOW ELEMENT / RESTRICTION ORIFICE (RO)
CENTRIFUGAL COMPRESSOR SECTION
PUMP
DCS INSTRUMENT (TRANSMITTER IMPLIED, SAME NUMBER)
SIS TRIP FUNCTION (LOGIC SOLVER SEPARATE FROM DCS)
LEADER: SIS ON A DCS BUBBLE SHARES ITS TRANSMITTER
INSTRUMENT SIGNAL (ONLY TRIP / SOLENOID LINKS DRAWN)
PROCESS GAS LINE
UTILITY / DRAIN / RELIEF / FUEL LINE
CONNECTION (TEE)
CROSSING WITHOUT CONNECTION (VERTICAL JUMPS)
LINE NUMBER DNxxx-SVC-nnn · SERVICE CODES
PG PROCESS GAS · EG EXPORT GAS · FG FUEL GAS · FL FLARE
CD CLOSED DRAIN · CM COOLING MEDIUM · STREAM n = PFD / PROCESS TAB
INTERLOCK SCHEDULE (SIS) · FROM THE OTS C&E DATA
TAG
CAUSE
TRIP SET
DELAY
PRE-ALARM
ACTS
ESD-1
ESD PUSH-BUTTON (CCR)
—
0 s
—
I-1
ESD-2
ESD PUSH-BUTTON + BLOWDOWN
—
0 s
—
I-2
LSHH-101
V-101 LEVEL
≥ 85 %
3 s
65 %
I-1
LSHH-107
V-102 LEVEL
≥ 85 %
3 s
65 %
I-1
TSHH-104
SECTION 1 DISCH. TEMP.
≥ 150 °C
3 s
125 °C
I-1
TSHH-109
SECTION 2 DISCH. TEMP.
≥ 150 °C
3 s
130 °C
I-1
VSHH-105
SECTION 1 VIBRATION
≥ 90 µm
3 s
60 µm
I-1
VSHH-110
SECTION 2 VIBRATION
≥ 90 µm
3 s
60 µm
I-1
PSLL-150
LUBE-OIL HEADER (TURNING)
≤ 1.2 barg
2 s
1.8 barg
I-1
SSHH-100
OVERSPEED (SIC-100 SIGNAL)
≥ 110 %
0.5 s
104 %
I-1
PSHH-112
DISCHARGE HEADER
≥ 132 barg
2 s
126 barg
I-1
PSLL-101
SUCTION V-101 (RUN > 60 %)
≤ 20 barg
5 s
28.5 barg
I-1
GT-100
GT TRIP / FLAME-OUT
—
0 s
—
I-1
PSHH-001
PRODUCTION HEADER
≥ 34.5 barg
3 s
32.5 barg
XV-001
I-1 COMPRESSOR TRIP (PSD): XV-100 FUEL SHUT (GT COASTS DOWN), ESDV-101 + ESDV-113 SHUT,
UV-103 / UV-108 100 % OPEN (UIC TO MAN), PIC-101 + SIC-100 TO MAN (SIC OUT 0 %),
PIC-102 OUTPUT ≥ 80 % (PRODUCTION TO FLARE). LATCHED, FIRST-OUT ON THE SIS TAB.
I-2 = I-1 + BDV-101 / BDV-112 OPEN (RO 45 mm) + XV-001 SHUT (WELLS SHUT IN).
XV-001: PSHH-001 SHUTS THE WELLS ONLY (NO I-1); REOPEN BELOW 33.5 barg.
TRIPS ACT IN RUN / START; RESET REFUSED WHILE A CAUSE HOLDS OR SPEED > 5 %.
DESIGN POINT (OTS MODEL, NOTE 1) · SHAFT 16.69 MW · 9 500 rpm
SECTION
W kg/s
P IN barg
T IN °C
P OUT barg
T OUT °C
RATIO r
Q IN m³/s
Ep
POWER MW
SURGE q
1 (LP)
61.75
30.0
34.4
60.9
105.2
1.997
2.11
0.685
7.95
0.62
2 (HP)
60.26
60.4
40.0
121.6
115.7
1.997
1.00
0.655
8.30
0.62
GENERAL NOTES
1. DESIGN BASIS (ASSUMED FOR TRAINING, TBC): 200 MMSCFD (61.75 kg/s) GULF OF THAILAND GAS, MW 22.3 (CO2 12 %), γ 1.258; 30 → 120 barg; N = 2 SECTIONS,
r = 3.96^(1/2) = 1.99 EACH (ONE STAGE: T2 ≈ 192 °C > SEAL CEILING 150 °C). Ep FROM LECTURE CHART; T2 = T1·r^((γ−1)/(γ·Ep)). NUMBERS = OTS DESIGN POINT.
MASS BALANCE 61.75 IN = 60.25 EXPORT + 1.38 FUEL + 0.11 CONDENSATE (+0.005 ACCUMULATION) kg/s; V-101 LIQUIDS 0.22 kg/s ARRIVE WITH THE GAS.
2. LINE SIZES PRELIMINARY: VELOCITY AT DN BORE, CRITERIA v ≤ 20 m/s AND ρv² ≤ 15 000 Pa (ASSUMED); ALL ≤ 10.8 m/s AND ≤ 7 500 Pa. FLARE LINES: HOLD (FLARE STUDY).
3. SETTLE-OUT AFTER A TRIP ≈ 69 barg (MODEL): SUCTION SIDE (V-101, SECTION 1) DESIGN PRESSURE 80 barg (TBC). PSV-107 80 barg ON V-102 AND PSV-112 138 barg
ON THE DISCHARGE: HOLD (NOT DRAWN). BLOWDOWN COOLS BY EXPANSION: FLARE AND BLOWDOWN LINES LTCS, MDMT −46 °C (TBC).
4. UIC-103/108 SURGE MARGIN = (q/q_SURGE − 1)·100 % FROM FT, PT, TT; CONTROL LINE 10 %; FAST OPEN BELOW 5 %. UV-103/108 ALSO HAVE ZI-103/108 (POSITION).
5. CASCADE: PIC-101 (SUCTION) → SIC-100 SPEED SP (0–100 % = 70–105 %) → FV-100 FUEL. DCS SIGNAL LINES NOT DRAWN; EACH DCS BUBBLE HAS ITS OWN
TRANSMITTER (PT/TT/LT/FT/VT, SAME NUMBER, e.g. TT-106 FOR TIC-106). PSHH-001 SHARES PT-001 (PIC-102), PSLL-101 PT-101 (PIC-101), SSHH-100 THE SPEED PICK-UP.
6. FUEL GAS FROM V-102 OUTLET VIA FUEL-GAS SKID (PCV TO 25 barg, HEATER, FILTER NOT SHOWN). LUBE-OIL CONSOLE, SEAL-GAS PANEL, CM SYSTEM (P-160, TI-160): VENDOR / SEPARATE SHEETS.
7. DRAINS MV-130…133 TO CLOSED DRAIN, VENTS MV-134/135 BLINDED; ALL OTHER HIGH-POINT VENTS / LOW-POINT DRAINS DN25 (TYP., NOT SHOWN). INSTRUMENTS C/W ROOT & TEST VALVES.
OPERATING NOTES AND OPEN ITEMS
A. START-UP: PRESSURISE WITH HV-101 UNTIL ΔP ACROSS ESDV-101 ≤ 3 bar,
OPEN ESDV-101, START GT-100 ON FULL RECYCLE. GT PERMISSIVES: SIS READY,
PI-150 ≥ 2.0 barg, P-160 RUNNING, PI-101 ≥ 20 barg, UV-103/108 ≥ 90 %,
LEVELS < 60 %, BDVs SHUT.
B. AFTER A PSD THE LOOP SETTLES OUT: VENT WITH HV-102 TO HEADER PRESSURE
BEFORE REOPENING ESDV-101.
C. ANTI-SURGE, FLARE AND BLOWDOWN VALVES ARE CHOKED WHEN P2/P1 < 0.553.
D. P-150B STANDBY LUBE-OIL PUMP AUTO-STARTS AT PI-150 1.8 barg (BPCS).
E. HOLD / TBC: PSV-107, PSV-112, FLARE LINE SIZES, HV-101/102 FAIL POSITION
(FC ASSUMED), DESIGN PRESSURES, CM SIDE (E-101 7.3 MW, E-102 7.7 MW).
F. REV B = ALTERNATIVE VERSION (EPC STANDARD). REV A STAYS THE SCREEN
REFERENCE USED BY THE DCS, THE DECKS AND THE EXERCISES; SAME TAGS.
REV
DESCRIPTION
DATE
A
SCREEN REFERENCE USED BY THE DCS, DECKS AND EXERCISES
25-SEP-26
B
ALTERNATIVE VERSION, EPC STANDARD
12-OCT-26
CHEM ENG CHULALONGKORN UNIVERSITY · OTS
P&ID — GAS EXPORT COMPRESSOR K-100
ALTERNATIVE VERSION
DRAWN:
Apinan Soottitantawat
CHK'D: --
APP'D: --
DATE: 12-OCT-26
DWG NO.
KC-PID-100
REV
B
SCALE
N.T.S.
SHEET
1 OF 1