## Slide 1
C-201
27
18
8
1
SUMP
FEED FROM
UPSTREAM UNIT
6"-P-200
V-201
FEED SURGE DRUM
TI
201
LT
201
LIC
201
REV B: LI-201 LAL/LAH-201
REV C: LIC-201 → FIC-201 (NOTE 16)
RSP
LG-201
VENT
DR
MV-201
P-201A
MOTOR
NRV-201
MV-203
MV-202
P-201B
STEAM TURBINE (NOTE 7)
NRV-202
MV-204
6"-P-201
4"-P-202
XV-201
S
FE-201
FT
201
FSLL
201
AUTO-START P-201B
MV-205
MV-206
FV-201 FC
MV-207
BYPASS
FIC
201
E-201
FEED PREHEATER
6"-P-203
TRAY 18
TIC
202
LP STEAM 0.45 MPa g
6"-LS-301
HV-202
XV-202
S
FE-206
FI
206
TV-202 FC
T
ST-201
COND.
TIC
227
TRAY 27
PDI
212
NOTE 9
TI
242
TI
241
TI
246
TI
245
TI
243
TT
208
TIC
208
TRAY 8
LT
202
LIC
202
LS
202
LSLL
202
TI
209
8"-P-204
PSV-201
SET 1.80 MPa g
TO FLARE
4"x6"
PT
211
PI
211
PT
210
PIC
210
E-202 CONDENSER
10"-CW-401
10"-CW-402
CW RETURN
CW SUPPLY 15 °C
HV-216
FE-216
FI
216
TI
214
TI
215
6"-P-205
TI
213
V-202
REFLUX DRUM
1"-P-206
PV-210 FO
HV-210
FE-217
FI
217
TO FUEL GAS
0.40 MPa g
LS
203
LSHH
203
LT
203
LIC
203
MV-211
P-202A
MOTOR
NRV-211
MV-213
MV-212
P-202B
MOTOR
NRV-212
MV-214
6"-P-207
PDT
230
PDSL
230
AUTO-START P-202B
4"-P-208
TRAY 27
4"-P-209
FV-204 FO
FE-204
FT
204
FIC
204
NOTE 8
LV-203 FC
FE-203
FI
203
AI
219
C4+
PROPANE TO
STORAGE
E-203
REBOILER
(THERMOSYPHON)
8"-P-211
10"-P-212
LP STEAM
0.45 MPa g
6"-LS-302
HV-209
XV-209
S
TV-208 FC
FE-205
FI
205
PI
207
PI
205
T
ST-202
COND.
4"-P-210
DR
LV-202 FC
FE-202
FI
202
AI
220
C3
BOTTOMS TO
DEBUTANIZER
LEGEND
PROCESS LINE
UTILITY LINE (STEAM, COOLING WATER, RELIEF)
INSTRUMENT SIGNAL
MANUAL VALVE (GATE)
CONTROL VALVE, FO / FC = FAIL OPEN / CLOSED
S
SIS SHUT-OFF VALVE, SOLENOID, FAIL CLOSED
CHECK VALVE
FLOW ELEMENT (ORIFICE)
T
STEAM TRAP
RELIEF VALVE (PSV)
TI
201
FIELD-MOUNTED INSTRUMENT
FIC
201
DCS FUNCTION (OPERATOR CONSOLE)
LSHH
203
SIS FUNCTION
SERVICE CODES: P PROCESS HYDROCARBON · LS LP STEAM
CW COOLING WATER · DR DRAIN · COND. STEAM CONDENSATE
LINE NO. = SIZE - SERVICE - NUMBER (SIZES TBC, NOTE 2)
INTERLOCK SCHEDULE · SIS
TAG
CAUSE
SETTING
DELAY
LSLL-202
C-201 SUMP LOW-LOW *
< 5 %
5 s
LSHH-203
V-202 LEVEL HIGH-HIGH
> 92 %
5 s
HS-ESD
ESD PUSHBUTTON (DCS)
MANUAL
0 s
FSLL-201
LOW FEED FLOW **
< 15 m³/h
5 s
PDSL-230
LOW P-202 DIFF. PRESS.
< 150 kPa
3 s
PSV-201
C-201 OVERPRESSURE
1.80 MPa g
MECH.
EFFECTS:
LSLL-202: CLOSE XV-209 & XV-202; TIC-208, TIC-202 MAN 0 %.
LSHH-203 / HS-ESD: AS LSLL-202, PLUS CLOSE XV-201,
FIC-201 MAN 0 % (FEED STOPPED).
FSLL-201: AUTO-START P-201B (NOT A TRIP).
PDSL-230: AUTO-START P-202B (NOT A TRIP).
* ARMED ONLY WHEN SIS IS IN RUN (HEAT ON).
** ONLY WITH FV-201 > 20 % AND XV-201 OPEN.
RESET BLOCKED WHILE A CAUSE IS PRESENT. RE-OPEN XV-209
/ XV-202 NEEDS: FI-216 ≥ 250 m³/h, LIC-202 ≥ 30 %,
TIC-208 & TIC-202 MAN ≤ 10 %, HV-209 & HV-202 OPEN.
GENERAL NOTES:
1. DESIGN BASIS: DEPROPANIZER COLUMN VER 1 OTS MODEL, DESIGN CASE. PRESSURES MPa g. MW 44.1 / 58.1 kg/kmol ASSUMED.
FEED 60 m³/h ≈ 31.8 t/h (634 kmol/h, 57 mol-% C3), -1 → 75 °C IN E-201 (67 % VAPOUR), TRAY 18 OF 27.
PROPANE 32.1 m³/h ≈ 16.1 t/h; BOTTOMS 27.8 m³/h ≈ 15.6 t/h; VENT 72 Nm³/h. MASS CLOSURE +0.14 %.
TOP 1.70 / 45 °C, BOTTOM 109 °C, V-202 1.68, PUMP DISCH. P-201 2.36, P-202 2.26. E-201 3.50 MW (5.8 t/h LS),
E-203 2.24 MW (3.8 t/h LS), E-202 3.96 MW (CW 330 m³/h, 15 → 25 °C). OVERHEAD 40.8 t/h, 8 in AT 8.5 m/s.
2. LINE SIZES PRELIMINARY FROM VELOCITY (LIQUID 1-2.5 m/s, VAPOUR ≤ 10 m/s) - TBC BY HYDRAULIC CALCULATION.
3. PRESSURE INSTRUMENTS C/W ROOT AND TEST VALVES; PUMP CASING VENTS/DRAINS; TYP., NOT SHOWN.
4. XV-201, XV-202, XV-209 FAIL CLOSED, OPERATED BY THE SIS (SIGNALS NOT SHOWN). HV-202, HV-209 ARE MANUAL BLOCKS.
5. FAIL POSITIONS: FV-201, TV-202, TV-208, LV-202, LV-203 FC; FV-204 (REFLUX) AND PV-210 (VENT) FO.
6. LT-202 / LS-202 AND LT-203 / LS-203 ON SEPARATE NOZZLES; PT-211 INDEPENDENT OF PT-210 (PIC-210).
7. P-201A MOTOR, P-201B STEAM TURBINE (DIVERSE DRIVE); P-202A/B MOTOR. SPARE AUTO-STARTS (SCHEDULE).
NOTES (CONT.):
8. TIC-227 (TRAY 27) CAN CASCADE THE FIC-204 SET POINT (CAS); NORMALLY MAN, FIC-204 ON ITS OWN SET POINT. SIGNAL NOT SHOWN.
9. PDI-212 COLUMN DIFFERENTIAL PRESSURE, TAPS ABOVE TRAY 27 AND IN THE SUMP VAPOUR SPACE (FLOODING INDICATOR).
10. PSV-201 4L6, SET 1.80 MPa g: CW FAILURE 40 852 kg/h (API L ORIFICE); FIRE CASE TBC; 5.9 % OPERATING MARGIN - HOLD.
11. V-201 SHOWN WITHOUT OVERPRESSURE PROTECTION IN THE OTS SCOPE - PSV REQUIRED, HOLD.
12. PSHH ON C-201 OVERHEAD TO TRIP REBOILER STEAM BEFORE PSV LIFT RECOMMENDED - HOLD (NOT IN OTS SCOPE).
13. DCS INDICATORS (TI, PI, FI, AI) IMPLY A FIELD TRANSMITTER; AI-219 C4+ IN PROPANE, AI-220 C3 IN BOTTOMS.
14. ALARM SET POINTS: SEE WORKBOOK (ALARM TABLE); TRIP SET POINTS: INTERLOCK SCHEDULE.
15. TRAYS NUMBERED FROM THE BOTTOM; ONLY FEED, CONTROL AND INDICATION TRAYS ARE LABELLED.
16. DESIGN CASE (REV A): NO V-201 LEVEL CONTROL, LT-201 LOCAL. REV B: LI-201 ON DCS, LAL/LAH-201, FAL-201 ON FIC-201.
REV C: LIC-201 SETS THE FIC-201 SET POINT (CASCADE, RSP). BOTH ARE UPGRADES SELECTED IN THE OTS.
REV
DESCRIPTION
DATE
B
LI-201 ON DCS, LAL/LAH-201, FAL-201 (OPTION)
--
C
LIC-201 CASCADE; OTS SCREEN DWG (USED IN DECKS)
--
D
ALTERNATIVE VERSION, EPC STANDARD
30-SEP-26
DEPROPANIZER COLUMN VER 1 · OTS
P&ID — C-201 · ALTERNATIVE VERSION
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 30-SEP-26
DWG NO.
DC3-V1-PID-001
REV
D
SCALE
N.T.S.
SHEET
1 OF 1