## Slide 1
TK-101
Feed Tank
P-100 A/B
Feed Pumps
E-100
Feed Preheater
H-100
Natural-Draft Fired Heater
F-100
Air Intake Screen
NATURAL DRAFT FIRED HEATER VER 1 · OPERATOR TRAINING SIMULATOR
PROCESS FLOW DIAGRAM
H-100 NATURAL-DRAFT FIRED HEATER — FEED PREHEAT AND HEATING TO V-200
DRAWING No.
PFD-100
REV.
0
SIZE
A4
SHEET
1 OF 1
DRAWN
Apinan Soottitantawat
CHECKED
SCALE
NTS
DATE
2026-09-28
LEGEND
Mass Flow (kg/h)
Temperature (°C)
Pressure (kPa g)
Process Line
Utility Line
Control Valve
Process Input / Output
Stream Number
Line Crossing
Storage Tank
Centrifugal Pump
Heat Exchanger
Fired Heater
Filter
COMBUSTION
Fuel oil ~CH1.8, LHV 42 MJ/kg
Air ratio 1.11 (11 % excess), O2 ~2 %
Fired 2.84 MW; stack loss 17 %
NOTES
1. Flows in kg/h; temperatures in °C; pressures in kPa gauge.
2. Design case: feed 6.8 L/s (0.80 kg/L), duty 2.31 MW absorbed, efficiency 81.5 % (LHV).
3. Natural draft: no fan. Air drawn in through intake screen F-100 by stack draft.
4. Only the control valves that define the process are shown; see the P&ID tab for the rest.
V-200
1
2
19584
40
50
3
1030
4
19584
180
5
350
545
6
243
7
8
3892
20
9
4380
400
TK-101
P-100 A/B
E-100
hot fluid
H-100
F-100
Hot Fluid from Unit A
to Unit A
to Reactor V-200
Fuel Oil
Air
Flue Gas to Atmosphere
Hydrocarbon Feed