## Slide 1
M
R-101
PVC REACTOR (SEE PVC-PID-001)
JACKET 118 m2 WETTED, U 0.75 kW/m2K
BAFFLES 22 m2
CWS 32 C FROM CW SUPPLY HEADER
CWR TO COOLING TOWER
LS LP STEAM 3.5 barg
CWR
TI
120
FV-120
FO
FIC
120
TI
121
4"-CW-120
10"-CW-111 JACKET RETURN
TI
111
P-101A
P-101B
470 m3/h, ONE RUNNING
10"-CW-110 JACKET SUPPLY
PCV-112 BPR
4 barg (SPILL)
TV-110B
FO
TV-110A
FC
SM-101
TIC
110
FI
110
FSLL
110
TIC
100
R-101 TEMP.
(TE-100, PVC-PID-001)
SP (CASCADE)
TY-110
SPLIT
0-50 %
STEAM
50-100 %
CW
VPC
130
PV: TIC-110 OUT
SP: TV-110B 50 %
E-101
REFLUX CONDENSER
(SEE PVC-PID-001)
18"-VG-110 VCM VAPOUR / CONDENSATE
INERTS TO HV-135
(PVC-PID-001)
TI
131
FIC
130
FV-130
FO
SP HIGH LIMIT
12 m3/h PER % XI-100
8"-CW-130
LEGEND
PROCESS LINE
UTILITY LINE (CW, STEAM, N2)
SIGNAL LINE
LINE JUMP (NO JOIN)
CONTROL VALVE FO / FC
ON/OFF VALVE (SEQ. / SIS)
MANUAL VALVE
ORIFICE FLOW ELEMENT
TI
DCS INSTRUMENT
TI
FIELD INSTRUMENT
TI
SIS FUNCTION
DCS FUNCTION BLOCK
OFF-SHEET LINK
RELIEF VALVE
CONTROL LOOP SCHEDULE
LOOP
MEASURES
MOVES
FAIL
SET / NOTE
FIC-101
WATER CHARGE
FV-101
FC
240 m3/h, FQ 60 t
FIC-102
VCM CHARGE
FV-102
FC
180 t/h, FQ 51 t
LIC-100
R-101 LEVEL
FIC-103 SP
-
83 %
FIC-103
INJECTION WATER
FV-103
FC
CAS (~3 m3/h)
TIC-100
R-101 TEMP.
TIC-110 SP
-
57.0 C (K 67)
TIC-110
JACKET INLET
TY-110
-
CAS (~38 C)
TY-110
0-50 % OUT
TV-110A STEAM
FC
HEAT-UP
TY-110
50-100 % OUT
TV-110B CW
FO
COOLING
FIC-120
BAFFLE CW
FV-120
FO
80 m3/h
VPC-130
TIC-110 OUT
FIC-130 SP
-
50 % (NOTE 5)
FIC-130
E-101 CW
FV-130
FO
CAS
HIC-135
-
HV-135 INERTS
FC
MANUAL
HIC-105
-
PV-105 DEGAS
FC
END OF BATCH
SIS INTERLOCKS
I-
INITIATOR
SETTING
ACTION
1
TSHH-101 R-101 TEMP.
> 63 C, 10 s
A
2
PSHH-101 R-101 PRESS.
> 12.5 barg, 5 s
A
3
XS-101 AGITATOR STOP
REACTING, 15 s
A
4
FSLL-110 JACKET FLOW
< 120 m3/h, 30 s
A
5
LSHH-100 R-101 LEVEL
> 94 %, 5 s
B
6
HS-001 ESD PUSHBUTTON
MANUAL
A + XV-108
A = SHORT-STOP XV-104, CLOSE XV-101/102/103, FV-103 TO 0,
FORCE TV-110B / FV-120 / FV-130 OPEN. B = CLOSE XV-101/102, FV-103.
ITEM (OTS DESIGN POINT)
VALUE
WATER / VCM CHARGE
60 t (55 C) / 51 t (25 C)
REACTION
57.0 C, 8.6 barg
LEVEL / CONTENTS AT 2 h
83 % / 117.8 t
Q REACTION AT 2 h
2.71 MW (PEAK 3.43)
JACKET / BAFFLES / E-101
1.48 / 0.40 / 0.98 MW
END POINT
dP 1.8 bar, X 0.85
PVC PER BATCH / TIME
43.2 t / 5.3 h
GENERAL NOTES:
1. SEE PVC-PID-001 NOTES 1-3 FOR THE DESIGN BASIS AND RECIPE, NOTE 8 AND THE SIS TABLE FOR TRIPS. THIS SHEET SHOWS THE R-101 HEAT-REMOVAL SYSTEMS AND THE TEMPERATURE CONTROL.
2. JACKET: CLOSED TEMPERED-WATER LOOP, P-101A/B 470 m3/h (ONE RUNNING; B STARTED BY OPERATOR - AUTO-START TBC). CW 32 C INJECTED THROUGH TV-110B (FAIL OPEN) AND LP STEAM THROUGH TV-110A (FAIL CLOSED) + STEAM MIXER SM-101;
THE SAME MASS SPILLS TO CWR THROUGH BACK-PRESSURE REGULATOR PCV-112 (LOOP 4 barg). FSLL-110 < 120 m3/h FOR 30 s WHILE REACTING -> SIS I-4 (SHORT-STOP).
3. TEMPERATURE CONTROL: TIC-100 (MASTER, R-101 CONTENTS; Kc 10, Ti 1500 s, Td 120 s) SETS TIC-110 (SLAVE, JACKET INLET; Kc 2, Ti 40 s). TY-110 SPLIT RANGE: OUTPUT 0 % = FULL STEAM, 50 % = BOTH SHUT, 100 % = FULL CW.
4. VPC-130 = VALVE-POSITION CONTROL: HOLDS TV-110B NEAR 50 % OPEN BY RESETTING FIC-130, SO THE JACKET KEEPS ITS TRIM MARGIN AND THE REFLUX CONDENSER TAKES THE GROWING LOAD. FIC-130 SP HIGH LIMIT = 12 m3/h PER % OF XI-100
(ANTI-FOAM: TOO MUCH BOIL-UP BEFORE ~10 % CONVERSION CARRIES FOAM AND PVC INTO E-101).
5. BAFFLES: FOUR ADJUSTABLE WATER-COOLED BAFFLES (22 m2) ON ONCE-THROUGH CW, FIC-120 80 m3/h.
6. DESIGN DUTIES AT 2 h (X = 26 %): REACTION 2.71 MW + AGITATOR 0.29 MW = JACKET 1.48 + BAFFLES 0.40 + E-101 0.98 MW. PEAK REACTION 3.43 MW NEAR X = 0.7; THE JACKET ALONE (MAX ~1.8 MW) CANNOT CARRY IT - E-101 ADDS THE MISSING AREA.
7. CW SUPPLY 32 C (TROPICAL DESIGN). E-101 CW RETURN APPROACHES 55 C AT LOW FLOW: MINIMUM-FLOW / SCALING LIMIT TBC WITH THE CW TREATMENT VENDOR.
8. LINE SIZES AND MATERIALS PRELIMINARY - TBC BY PIPING. SERVICE CODES AS PVC-PID-001; LS = LP STEAM.
REV
DESCRIPTION
DATE
A
ISSUED FOR OTS DEVELOPMENT (REVIEW)
25-SEP-26
CHULA CHEM. ENG. - PVC REACTOR VER 1 (OTS)
P&ID - R-101 HEAT REMOVAL:
JACKET, BAFFLES, E-101 CW
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 25-SEP-26
DWG NO.
PVC-PID-002
REV
A
SCALE
N.T.S.
SHEET
2 OF 2