## Slide 1
P-100 A/B
Benzene Feed Pumps
R-101
Slurry Reactor +
Agitator M-101
E-103
Reflux Condenser
V-103
Reflux Drum
P-101 A/B
Pump-around Pumps
E-101
Pump-around Cooler /
LP Steam Generator
D-101
Steam Drum
R-102
Slurry Finishing
Reactor (jacketed)
P-102 A/B
R-102 Transfer Pumps
F-102 A/B
Catalyst Candle
Filters
R-103
Trickle-bed Finishing
Reactor
E-106
Product Cooler
V-104
HP Separator
K-101
Recycle H2 Compressor
CYCLOHEXANE REACTOR VER 1 · OPERATOR TRAINING SIMULATOR
PROCESS FLOW DIAGRAM
CYCLOHEXANE UNIT — BENZENE HYDROGENATION REACTOR TRAIN
DRAWING No.
CHX-V1-PFD-001
REV.
0
SIZE
A4
SHEET
1 OF 1
DRAWN
Apinan Soottitantawat
CHECKED
SCALE
NTS
DATE
2026-10-26
LEGEND
Mass Flow (t/h)
Temperature (°C)
Pressure (bar g)
Process Line
Utility Line
Control Valve
Process Input / Output
Stream Number
Line Crossing
Centrifugal Pump
Stirred Reactor
Heat Exchanger
Separator
Vessel / Drum
Filter
Packed-Bed Reactor
Compressor
REACTION
C6H6 + 3 H2 -> C6H12 dH = -206 kJ/mol
Raney-Ni slurry (R-101/102), Ni bed (R-103)
Benzene 34.8 t/h; product 37.5 t/h, 2 ppm benzene
NOTES
1. Rev 0 · Issued for teaching. Flags: t/h, °C, bar g at the design point.
2. All numbers come from the simulator model (design state, noise off); no flag = no model value.
3. H2 passes R-101, E-103/V-103, R-102, R-103, V-104 and K-101 in series; D-101 blowdown (≈1 %) not shown.
1
2
34.8
40
30
3
6.42
60
32
4
51.3
200
30
5
6
46.5
55.7
30
7
4.73
55.7
29.6
8
36.5
200
30
9
10
357.3
200
32
11
357.3
159.3
12
20.3
160
29.6
13
14
15
20.9
160
29.3
16
41.2
158.6
29.3
17
18
6.42
44.9
29
19
2.98
40
35
20
0.28
44.9
29
21
37.5
44.9
29
22
14.7
155.8
4.5
23
14.9
105
10
P-100 A/B
R-101
E-103
cw
V-103
P-101 A/B
E-101
bfw
D-101
R-102
P-102 A/B
F-102 A/B
R-103
E-106
cw
V-104
K-101
Benzene from TK-100
Make-up H2
Purge to Fuel Gas
Cyclohexane to TK-106 / TK-107
BFW
LP Steam
MP Steam / CW (jacket)
Recycle H2
Reflux