## Slide 1
BENZENE 99.9 %
FROM TK-100 (OSBL)
S
FC
EIV-100*
6"-P-1001
MV-301
NO
P-100A
NRV-100A*
MV-302
NO
MV-303
NO
P-100B
NRV-100B*
MV-304
NO
DR
MV-305
NC
4"-P-1002
FE-101
FT
101
FIC
101
MV-306
NO
MV-307
NO
MV-308
NC
FC
FV-101
S
FC
XV-101
START-UP CYCLOHEXANE
FROM STORAGE (OSBL)
HV-116
NC
NRV-301
6"-P-1003
R-101
SLURRY
REACTOR
RANEY-Ni
M
M-101
D-102
CAT. POT
HV-117
NC
4"-SL-1004
TE-100
TT
100
TI
100
TE-101
TT
101
TIC
101
TSHH
100
10"-P-1005
PT
101
PI
101
PSHH
101
PSV-101*
SET 36 bar g
TO FLARE HEADER (V-190*)
6"-FL-1040
E-103
REFLUX CONDENSER
CWS
CWR
HV-113
NO
MV-309
LO
10"-CW-1030
TSV-113*
6"-P-1006
TT
103
TI
103
V-103
REFLUX
DRUM
LG
103
6"-G-1008
TO R-102
SHT 2
6"-P-1007
FT
105
FI
105
FE-105
DR
MV-310
NC
JT
101
JI
101
XS
101
SSL
101*
TO R-102
SHT 2
6"-SL-1014
MV-311
NO
MV-312
NO
MV-313
NC
FC
LV-101
LT
101
LIC
101
FROM K-101
SHT 2
8"-G-1009
FE-103
FT
103
FIC
103
MV-314
NO
MV-315
NO
MV-316
NC
FC
FV-103
S
FC
EIV-101*
18"-SL-1010
MV-317
NO
P-101A
NRV-302
MV-318
NO
MV-319
NO
P-101B
NRV-303
MV-320
NO
DR
MV-321
NC
16"-SL-1011
FO
FV-104
FT
104
FIC
104
12"-SL-1015
16"-SL-1013
16"-SL-1016
TE-104
12"-SL-1012
TT
104
TI
104
E-101
PUMP-AROUND COOLER
LP STEAM GEN.
D-101
STEAM DRUM
FO
HY-101A
FO
HY-101B
12"-BW-1022
14"-LS-1023
ATM
PSV-109*
8 bar g
LP STEAM
HEADER
10"-LS-1021
FO
PV-110
FT
111
FI
111
PT
110
PIC
110
BFW 105 °C
3"-BW-1020
FO
LV-109
FT
109
FI
109
LT
109
LIC
109
MV-322 THR.
BD
MP STEAM
10 bar g
HV-110
NC
FC
HY-101D
8"-MS-1024
T
ST-101
FC
HY-101C
3"-CD-1025 TO CONDENSATE
HS
101
TO HY-101A/B/C/D
DESIGN CASE (OTS MODEL)
TAG
VALUE
BENZENE FEED
FIC-101
34.8 t/h · 40 °C
H2 TO R-101 SPARGER
FIC-103
46,000 Nm³/h · 60 °C
R-101 TEMPERATURE
TIC-101 / TI-100
200.0 °C
R-101 PRESSURE
PI-101
30.00 bar g
R-101 LEVEL
LIC-101
65 %
AGITATOR POWER
JI-101
153 kW
PUMP-AROUND THROUGH E-101
FIC-104
357 t/h (pump 606)
E-101 RETURN / DUTY
TI-104
159.3 °C · 9.6 MW
REFLUX / E-103 OUTLET
FI-105 / TI-103
46.5 t/h · 55.7 °C
OVERFLOW TO R-102
LV-101
36.5 t/h · 200 °C
D-101 PRESSURE / LEVEL
PIC-110 / LIC-109
4.50 bar g · 50 %
LP STEAM / BFW
FI-111 / FI-109
14.7 / 14.9 t/h
R-101 BOILING POINT AT 30 bar g
—
258 °C (ceiling)
LEGEND
MAIN PROCESS LINE
UTILITY / SECONDARY / BYPASS LINE
INSTRUMENT PROCESS CONNECTION
ELECTRONIC SIGNAL (4-20 mA / BUS)
CROSSING WITHOUT CONNECTION (VERTICAL JUMPS) / TEE
TT
nnn
FIELD INSTRUMENT (TRANSMITTER, SWITCH)
TIC
nnn
DCS FUNCTION (INDICATION, CONTROL, ALARM)
TSHH
nnn
SIS FUNCTION (LOGIC SOLVER SIS-100)
FC
CONTROL VALVE, DIAPHRAGM ACTUATOR;
FAIL POSITION FC CLOSED / FO OPEN
S
FC
ON/OFF VALVE WITH SOLENOID (SIS, EIV, HY)
FO
THREE-WAY CONTROL VALVE
MANUAL GATE VALVE (NO / NC / LO = NORMALLY
OPEN / CLOSED / LOCKED OPEN)
MANUAL GLOBE VALVE (BYPASS, THROTTLING)
CHECK VALVE (FLOW LEFT TO RIGHT)
SAFETY / THERMAL RELIEF VALVE
FLOW ELEMENT (ORIFICE)
DRAIN (DR) / VENT (V) VALVE WITH CAP
T
STEAM TRAP
OFF-PAGE CONNECTOR (SHEET REFERENCE BESIDE IT)
LINE NUMBER: SIZE"-SERVICE-NNNN (e.g. 8"-G-1009)
SERVICE: P PROCESS LIQUID / TWO-PHASE · G HYDROGEN GAS
SL SLURRY (Raney-Ni) · BW BOILER FEED WATER · LS LP STEAM
MS MP STEAM · CD CONDENSATE · BD BLOWDOWN · CW COOLING
WATER · FL FLARE · N NITROGEN. NNNN: 1nnn SHEET 1, 2nnn SHEET 2
TAGS: MV MANUAL VALVE · NRV CHECK VALVE · HV OPERATOR
HAND VALVE OF THE OTS · HY VALVE MOVED BY A DCS SELECTOR
* = RECOMMENDED ADDITION (SAFETY LAYERS TAB, SL-Rn);
NOT IN THE OTS MODEL: HOLD FOR APPROVAL
NOTES:
1 DESIGN CASE = OTS MODEL AT DESIGN, NOISE OFF: benzene 34.8 t/h (0.1238 kmol/s), R-101 200 °C / 30.0 bar g, 98 % conversion in R-101,
E-101 9.6 MW raising 14.7 t/h LP steam at 4.5 bar g, boil-up condensed in E-103 and refluxed (46.5 t/h at 55.7 °C). Balances checked in
eng_check.py before drawing: total 37.78 t/h in = out (+0.01 %), H2 and CH4 within 0.01 %, R-101 heat 25.2 MW generated vs 25.1 MW
removed (−0.4 %), D-101 BFW = steam + 1 % blowdown.
2 LINE SIZES ARE PRELIMINARY, FROM VELOCITY (liquid suction ≤ 1–2 m/s, discharge ≤ 2–2.5 m/s, gas ≤ 12–15 m/s, steam ≤ 30 m/s; typical
practice). TBC by hydraulic calculation; pipe classes not assigned (HOLD).
3 HYDROGEN LOOP DESIGN PRESSURE 36 bar g (assumed, Safety layers tab) = PSV-101 set; R-101 design temperature 250 °C (assumed). Relief
loads not calculated (HOLD).
4 FIELD TRANSMITTERS (circle) are wired to the DCS (circle with bar) and, where drawn, separately to the SIS logic solver SIS-100 (circle
in square). SIS outputs to XV / EIV solenoids and motor starters are not drawn: see the interlock schedule on sheet 2.
5 TE-100 / TT-100 (SIS) and TE-101 / TT-101 (BPCS) are separate elements in separate thermowells. TIC-101 is the master of FIC-104
(cascade). FV-104 is three-way: the rest of the P-101 flow bypasses E-101.
6 HS-101 (DCS selector) COOL: HY-101A/B open (E-101 shell on the D-101 thermosyphon), HY-101C/D shut. HEAT: HY-101A/B shut, HY-101C/D open,
MP steam set by the operator on HV-110. A unit trip forces COOL (HY-101D shuts the MP steam: in the OTS model the trip closes HV-110).
HY-101A-D and ST-101 are new tags of this drawing (HOLD: arrangement TBC).
7 ITEMS MARKED * are recommended additions from the Safety layers tab (SL-Rn), not in the OTS model: HOLD. Further SRS / LOPA
recommendations not drawn: LSLL-101 on LT-101S, FSLL-103 on FT-103S, AT-100B, XV-105B, TSHH-107S on TE-107S, PIAH-101 (32.5 bar g on
PT-101), TDA-101 (TT-100 vs TT-101).
8 MV-3nn and NRV-3nn are new numbers of this drawing (sheet 2: MV-4nn, NRV-4nn). Every pump has suction and discharge isolation and a
discharge check valve. Pressure and level instruments c/w root, isolation and test valves (typ., not shown).
9 R-101 has no vent of its own: it is vented through E-103 / V-103 and the R-102 off-gas line to flare (HV-121, EDV-101, sheet 2). No
isolation valve between R-101 and PSV-101.
10 Raney-Ni is pyrophoric: D-102 charged under liquid with an N2 blanket (CAT-1); HV-117 is opened only with D-102 full of liquid.
11 THE SCREEN P&ID OF THE OTS PAGE stays the reference for the DCS, the decks and the exercises. Where this drawing places an instrument
differently it is listed as a difference (P&ID tab, alternative version, part 5), not as an error.
REV
DESCRIPTION
DATE
—
SCREEN P&ID IN OTS PAGE: CURRENT, USED IN DECKS
0
ISSUED FOR TEACHING · ALT. VERSION, EPC STD
2026-10-26
CYCLOHEXANE REACTOR VER 1 — OTS TEACHING UNIT
P&ID — CYCLOHEXANE REACTOR VER 1 · ALTERNATIVE VERSION
SHEET 1: FEED · R-101 · E-101/D-101 · E-103/V-103
DRAWN: Apinan Soottitantawat
CHK'D
—
APP'D
—
DATE
2026-10-26
DWG NO.
CHX-V1-PID-001
REV
0
SCALE
N.T.S.
SHEET
1 OF 2