## Slide 1
TO FLARE
V-190*
8"-FL-2016
R-102
SLURRY
FINISHING
REACTOR
160 °C
M
M-102
JACKET
GAS FROM V-103
SHT 1
6"-G-1008
SLURRY FROM LV-101
SHT 1
6"-SL-1014
CWR
CONDENSATE
MP STEAM 10 bar g
CWS 32 °C
FO
HY-102C
T
ST-102
FC
HY-102D
6"-CW-2022
2"-CD-2023
TSV-102J*
FC
HY-102A
FO
HY-102B
FT
108
FI
108
FC
TV-102
HS
102
TO HY-102A/B/C/D
8"-P-2004
PT
102
PI
102
TT
102
TIC
102
LT
102
LIC
102
PSV-102*
36 bar g
S
FO
EDV-101
HV-121
NC
4"-FL-2015 TO FLARE
TE-106
TT
106
TI
106
S
FC
EIV-102*
6"-SL-2001
MV-401
NO
P-102A
NRV-401
MV-402
NO
MV-403
NO
P-102B
NRV-402
MV-404
NO
DR
MV-405
NC
3"-SL-2002
MV-406
NO
MV-407
NO
MV-408
NC
MV-409
NC
F-102A/B
PDT
102
PDI
102
MV-410
NO
MV-411
NO
MV-412
NC
FC
LV-102
3"-P-2003
FE-102
FT
102
FI
102
CANDLE FILTERS; TSV-102F* ON EACH,
SET 36 bar g → CLOSED DRAIN (TYP.)
R-103
TRICKLE
BED
Ni/Al2O3
TT
107A
TI
107A
TT
107B
TI
107B
TT
107C
TI
107C
TT
107D
TI
107D
TT
107E
TI
107E
TSHH
107
TE-107A…E
10"-P-2005
E-106
PRODUCT COOLER
8"-P-2006
CWS
MV-413
NO
CWR
MV-414
LO
10"-CW-2030
TSV-106* (10 bar g)
ON CW OUTLET
V-104
HP SEPARATOR
PSV-104*
36 bar g
10"-G-2007
MAKE-UP H2
35 bar g
S
FC
XV-105
FT
106
FI
106
MV-415
NO
MV-416
NO
MV-417
NC
FC
PV-105
8"-G-2009
PT
105
PIC
105
N2 8 bar g
HV-120
NC
NRV-403
2"-N-2014
FUEL GAS
FC
HV-107
FT
107
FI
107
HIC
107
2"-G-2010
K-101
M
RECYCLE H2
COMPRESSOR
XS
102
NRV-112*
MV-418
NO
TO FV-103
SHT 1
8"-G-2008
PT
112
PI
112
AT
100
AI
100
AT
105
AI
105
PSV-112*
42 bar g
LT
104
LT
104S
LIC
104
LSHH
104
LSLL
104*
TT
109
TI
109
S
FC
EIV-104*
S
FC
XV-104*
MV-419
NO
MV-420
NO
MV-421
NC
FC
LV-104
FT
110
FI
110
AT
103
AI
103
AI
104
6"-P-2011
FC
HY-115A
FO
HY-115B
TO TK-106
(ON SPEC)
TO TK-107
(SLOP)
6"-P-2012
6"-P-2013
HS
115
TO HY-115A/B
INTERLOCK SCHEDULE (SIS-100)
from model.js: tripConditions(), TRIPDLY, bmsTrip(), bmsCmd(); legend on sheet 1
TRIP
CAUSE / SENSOR
SETTING
DELAY
ACTION
TSHH-100
R-101 temperature,
TE-100 / TT-100
> 220 °C
5 s
UNIT TRIP
TSHH-107
R-103 bed, hottest of
TE-107A…E
> 220 °C
5 s
UNIT TRIP
PSHH-101
R-101 pressure, PT-101
> 33.5 bar g
3 s
UNIT TRIP
XS-101
M-101 stopped while
XV-101 open (run signal)
motor
stopped
10 s
UNIT TRIP
XS-102
K-101 stopped while
XV-101 open (run signal)
motor
stopped
10 s
UNIT TRIP
LSHH-104
V-104 level, LT-104S
(liquid toward K-101)
> 90 %
5 s
STOP K-101 ONLY
(not latched)
HS-100
ESD pushbutton
(operator)
manual
—
UNIT TRIP +
EDV-101 OPENS
LSLL-104*
V-104 level, LT-104S
(gas blow-by)
5 %
(assumed)
TBC
XV-104* SHUTS
(SL-R6, HOLD)
LSLL-109*
D-101 level
(own element, HOLD)
10 %
(assumed)
TBC
UNIT TRIP
(SL-R3, HOLD)
UNIT TRIP ACTIONS (bmsTrip, latched, first-out recorded):
• XV-101 benzene and XV-105 make-up H2 close (de-energise).
• K-101 stops.
• FIC-101, FIC-103, PIC-105 to MAN, output 0 %: FV-101, FV-103,
PV-105 close behind the SIS valves.
• HS-101 → COOL: HY-101A/B open, HY-101C/D shut (MP steam off);
FV-104 forced 100 % (full pump-around through E-101).
• HS-102 → COOL: HY-102B/C open, HY-102A/D shut; TV-102 100 %.
• ESD (HS-100) only: EDV-101 opens to flare.
• Recommended (SL-R7, HOLD): stop P-100A/B on unit trip.
RESET (bmsCmd reset):
• Blocked while a process trip condition is active or TI-100 > 210 °C.
• After reset H2 and benzene stay isolated until admitted again.
PERMISSIVES (purgePermissives, bmsCmd h2 / feed):
• XV-105 (H2) may open only with loop O2 AI-100 < 1 %.
• XV-101 (benzene) may open only with ALL of:
SIS reset, no trip latched · XV-105 open and AI-105 ≥ 80 % ·
LIC-101 ≥ 40 % · M-101 running · K-101 running and
FIC-103 ≥ 15 000 Nm³/h · TI-100 ≥ 140 °C (light-off) ·
E-103 on CW (HV-113 open).
FAIL POSITIONS ON INSTRUMENT AIR FAILURE (step() FAIL map):
• FC: FV-101, FV-103, PV-105, LV-101, TV-102, LV-102, LV-104, HV-107.
• FO: FV-104 (full flow through E-101), LV-109 (BFW), PV-110 (LP steam).
• SIS valves XV-101, XV-105, XV-104*, EIV-1nn* FC; EDV-101 FO (assumed).
• HY valves: fail to the COOL line-up (HY-101A/B, HY-102B/C FO).
NOTES:
1 DESIGN CASE (OTS model at design): R-102 160 °C / 29.60 bar g, level 55 %, jacket on MP steam 2.33 t/h (HS-102 HEAT); liquid to R-103
20.9 t/h, F-102 ΔP 0.26 bar (alarm 0.8); R-103 bed 158.5-158.6 °C; V-104 29.0 bar g / 44.9 °C, level 50 %; product 37.5 t/h, benzene 2.0
ppm, MCP 60 ppm; recycle 46,000 Nm³/h at 92.1 % H2; make-up 31,974 Nm³/h; purge 2,017 Nm³/h (HIC-107 25 %); K-101 discharge 32.0 bar g.
2 Loop pressure profile (model): K-101 32.0 → R-101 30.0 → R-102 29.6 → R-103 29.25 → V-104 29.0 bar g. K-101 discharge 57 °C by isentropic
compression (η 0.70 assumed) vs 60 °C in the model.
3 PSV-102*, PSV-104* set 36 bar g = loop design pressure (assumed); PSV-112* set 42 bar g (K-101 deadhead 35 × 1.154 = 40.4 bar g);
TSV-102J*, TSV-106* 10 bar g; TSV-102F* 36 bar g. Relief loads and flare header size: HOLD. V-190* flare knock-out drum is off this
drawing.
4 Line sizes preliminary (see sheet 1 note 2). Instrument and SIS conventions, MV / NRV numbering and the * mark: see sheet 1 legend and
notes.
5 PT-105 is on the V-104 gas outlet to K-101 (same pressure as V-104). TT-109 is on V-104. TE-107A…E are shared by TI-107A…E and TSHH-107
(separate SIS elements TE-107S: SRS recommendation, HOLD).
6 F-102A in service (inlet / outlet MVs open), F-102B on stand-by (shut, drained). Change-over: open B outlet, then B inlet, shut A inlet,
then A outlet; A is drained under N2 and kept wet (spent Raney-Ni is pyrophoric, CAT-2).
7 HS-102 (DCS selector) HEAT: HY-102A (MP steam) and HY-102D (condensate) open; COOL: HY-102B (CWS) and HY-102C (CWR) open. TIC-102 acts
reverse in HEAT and direct in COOL (model). HY-102A-D and ST-102 are new tags of this drawing (HOLD).
8 HS-115 (DCS) selects HY-115A to TK-106 (on spec) or HY-115B to TK-107 (slop). New tags; fail positions TBC (drawn: TK-107 open on air
failure).
9 K-101 minimum-flow / anti-surge protection and seal system not drawn (HOLD: vendor package). The OTS alarms "K-101 LOFL" when FV-103 is
shut with K-101 running.
10 N2 (HV-120) purges the loop below 1 % O2 before XV-105 opens; HV-121 vents to flare. EDV-101 is opened only by the ESD (HS-100) or by
hand from the SIS page.
11 TI-120 (CW supply temperature, page indicator) is measured on the CW header OSBL and is not drawn; TI-107 (hottest bed temperature) is a
DCS calculation from TT-107A…E.
REV
DESCRIPTION
DATE
—
SCREEN P&ID IN OTS PAGE: CURRENT, USED IN DECKS
0
ISSUED FOR TEACHING · ALT. VERSION, EPC STD
2026-10-26
CYCLOHEXANE REACTOR VER 1 — OTS TEACHING UNIT
P&ID — CYCLOHEXANE REACTOR VER 1 · ALTERNATIVE VERSION
SHEET 2: R-102 · R-103 · V-104 · K-101 · INTERLOCKS
DRAWN: Apinan Soottitantawat
CHK'D
—
APP'D
—
DATE
2026-10-26
DWG NO.
CHX-V1-PID-001
REV
0
SCALE
N.T.S.
SHEET
2 OF 2