## Slide 1
FROM E-201 HOT
SIDE (PID-001)
EFFLUENT ~206 C
E-202
FEED/EFFLUENT INTERCHANGER
(COLD)
TI
252
E-203
FINAL COOLER (CW)
CWS 32 C
CWR
TI
254
TI
253
DEMISTER
NLL 50 %
V-201
HP SEPARATOR
40 C, 75 bar g
PIC
203
PSHH
203
LSHH
204
LIC
204
I-4
I-3
DN900-PG-205
PV-203
FC
FI
203
DN150-PU-203
PURGE GAS TO REFORMER
FUEL HEADER
TO FLARE
PSV-201
SET 88 bar g
HV-205 (BD)
LV-204
FC
FI
209
DN200-CM-209
CRUDE METHANOL TO
LET-DOWN / DISTILLATION
MAKE-UP SYNGAS FROM
SYNGAS COMPRESSOR
86 bar a, 40 C
FIC
202
S
XV-202
SIS I-1...5
FV-202
FC
DN300-SG-202
M
C-201
LOOP CIRCULATOR
(VARIABLE SPEED)
FIC
201
FSLL
201
I-2
DN750-PG-202
TI
202
TO R-201 FEED AND
QUENCH HEADER
(MEOH-PID-001) ~97 C
TI
203
PI
201
LEGEND
PROCESS LINE
UTILITY LINE
SIGNAL LINE
LINE JUMP (NO JOIN)
CONTROL VALVE FO/FC
SIS SHUT-OFF VALVE
MANUAL VALVE
ORIFICE ELEMENT
TI
DCS INSTRUMENT
TI
FIELD INSTRUMENT
TI
SIS FUNCTION
OFF-SHEET LINK
CATALYST BED
QUENCH DISTRIBUTOR
CONTROL LOOP SCHEDULE
LOOP
MEASURES
MOVES
FAIL
SET / NOTE
FIC-201
CONVERTER FEED
C-201 SPEED (SC)
-
1928 kNm3/h
FIC-202
MAKE-UP SYNGAS
FV-202
FC
366 kNm3/h (RATE)
PIC-203
LOOP PRESS. V-201
PV-203 PURGE
FC
75.0 bar g
LIC-204
V-201 LEVEL
LV-204
FC
50 %
TIC-211
BED 1 INLET
TV-211 (E-201 BYP.)
FO
220 C
TIC-221
BED 2 INLET
TV-221 QUENCH 2
FO
225 C
TIC-231
BED 3 INLET
TV-231 QUENCH 3
FO
230 C
TIC-241
BED 4 INLET
TV-241 QUENCH 4
FO
235 C
HIC-214
-
E-204 STEAM
FC
START-UP ONLY
SIS INTERLOCKS (ACTION: MAKE-UP CUT)
I-
INITIATOR
SETTING
ACTION
1
TSHH-2xx ANY BED TC
> 300 C, 5 s
XV-202 + E-204 OFF
2
FSLL-201 CIRCULATION
< 45 %, 5 s *
XV-202 + E-204 OFF
3
LSHH-204 V-201 LEVEL
> 90 %, 5 s
XV-202 + STOP C-201
4
PSHH-203 LOOP PRESS.
> 85 bar g, 5 s
XV-202 + E-204 OFF
5
HS-200 ESD PUSHBUTTON
MANUAL
XV-202 + C-201 + E-204
DESIGN POINT (OTS MODEL)
BED
IN C
OUT C
MeOH %
CAT. t
1
220
260
2.1
25.0
2
225
277
3.6
41.7
3
230
270
4.4
58.3
4
235
268
4.8
83.3
CONVERTER 80 bar g IN; V-201 75 bar g / 40 C; FEED 1928 kNm3/h;
MAKE-UP 366 kNm3/h; PURGE 105 kNm3/h; MeOH 112.5 t/h; Q(RXN) 85 MW.
* ARMED ONLY WITH XV-202 OPEN.
GENERAL NOTES:
1. SEE MEOH-PID-001 NOTES 1-2 FOR DESIGN BASIS, LINE SIZING AND SERVICE CODES. LOOP GAS AT C-201 SUCTION: H2 81.6 / CH4 11.5 / CO2 2.5 / CO 2.3 / N2 1.7 / CH3OH 0.36 mol % (OTS MODEL).
2. MAKE-UP SYNGAS (BATTERY LIMIT): H2 73 / CO 16 / CO2 7 / CH4 3.3 / N2 0.5 / H2O 0.2 mol % (ASSUMED, TBC); FIC-202 SETS THE PLANT RATE; XV-202 FAILS CLOSED AND IS THE SIS FINAL ELEMENT FOR I-1...I-5.
3. PIC-203 HOLDS THE LOOP PRESSURE WITH THE PURGE (PV-203): A LESS ACTIVE CONVERTER OR A HOTTER SEPARATOR RAISES THE LOOP PRESSURE AND THE PURGE - THE PURGE RATE IS THE BEST CONVERTER HEALTH SIGNAL.
4. C-201: VARIABLE-SPEED MOTOR DRIVE; FIC-201 TRIMS SPEED. FSLL-201 (I-2) AND LSHH-204 (I-3, ALSO STOPS C-201 TO PROTECT IT FROM LIQUID CARRY-OVER). SEAL/LUBE SYSTEMS PER VENDOR.
5. E-203: COOLING WATER 32 C SUPPLY; V-201 AT 40 C CONDENSES CRUDE METHANOL (~85 wt % CH3OH); HIGHER SEPARATOR TEMPERATURE RECYCLES MORE CH3OH AND LOWERS CONVERTER DRIVING FORCE.
6. PSV-201 SET 88 bar g PROTECTS THE WHOLE LOOP (BLOCKED-OUTLET CASE AT MAX MAKE-UP - SIZING TBC). HV-205 MANUAL BLOWDOWN TO FLARE FOR EMERGENCY DEPRESSURING (RESTRICTION ORIFICE TBC).
REV
DESCRIPTION
DATE
A
ISSUED FOR OTS DEVELOPMENT (REVIEW)
25-SEP-26
CHULA CHEM. ENG. - METHANOL CONVERTER VER 1 (OTS)
P&ID - SYNTHESIS LOOP: C-201,
E-202, E-203, SEPARATOR V-201
DRAWN: APINAN
SOOTTITANTAWAT
CHK'D: --
APP'D: --
DATE: 25-SEP-26
DWG NO.
MEOH-PID-002
REV
A
SCALE
N.T.S.
SHEET
2 OF 2