## Slide 1
C-101
PACKED COLUMN
STRUCTURED PACKING
20 THEOR. STAGES, 2 BEDS
ID 150 mm × 4 m (TBC)
DESIGN FV / 1.0 barg (TBC)
TT
104
TI
104
ST 6
TT
103
TI
103
ST 13
TT
102
TI
102
ST 20
PDT
103
PDI
103
HP
LP
PT
103
PI
103
DN40-PV-101
PT
102
PIC
102
PSHH
102
TO PV-102
PT
102B
PT-102B REC. (HOLD)
PSV-101 REC. (HOLD)
SET 1.0 barg ASSUMED, TO SAFE LOC.
D-101
BATCH STILL (POT) 150 L
CHARGE 110 L = 95.7 kg
DESIGN FV / 1.0 barg (TBC)
TT
106
TIC
101
TT
101B
TSHH
101
TE-101B
LT
101
LI
101
LSLL
101
LT
101B
REC. (HOLD),
OWN NOZZLES
RD-102 + PSV-102 REC. (HOLD)
SET 1.0 barg ASSUMED, TO SAFE LOC.
FAME CHARGE 110 L FROM IBC
(HOSE CONNECTION, METHOD TBC)
DN25-PL-112
V-101
NRV-112
HV-201
V-102
RESIDUE (C18-RICH) TO STORAGE
DRAIN BELOW 60 °C (TBC)
DN25-PL-113
D-102
REBOILER, HOT OIL IN TUBES
DN25-PL-114
V-103
DR
DN40-PL-115
TT
101
TI
101
HOT OIL SUPPLY 290 °C
FROM VBD-PID-002 (TV-101)
DN25-HO-116
HOT OIL RETURN 256 °C
TO VBD-PID-002 (TT-108)
DN25-HO-117
E-103
OVERHEAD CONDENSER, TW IN TUBES
LOAD 2.37 kW (DESIGN), AREA TBC
TEMPERED WATER RETURN
TO VBD-PID-002
DN25-TW-119
TEMPERED WATER 60 °C, 1.2 m³/h
FROM VBD-PID-002 (HV-105)
DN25-TW-118
DN25-PL-102
TT
105
TI
105
D-104
REFLUX DRUM 4 L
DESIGN FV (TBC)
LT
104
LIC
104
LSLL
104
STOPS P-104
RY
104
SETS SP OF
FIC-104/105
DN25-VG-108
DN15-PL-103
V-110
P-104
NRV-104
V-111
DN15-PL-104
FT
104
FIC
104
FV-104
FO
FC
FV-105
FT
105
FIC
105
DN15-PL-105
V-115
D-105 SAMPLE PT.
S
XV-107
HS
107
CLOSED / TK-201 / TK-202
FAIL: STAYS PUT (ASSUMED)
DN15-PL-106
DN15-PL-107
TK-201
OFF-CUT
RECEIVER
VOLUME TBC
WT
201
WI
201
LOAD CELLS
V-116
TO PRODUCT DRUMS
VENT / EQUALISE
TO VACUUM (TBC)
TK-202
PRODUCT
RECEIVER
VOLUME TBC
WT
202
WI
202
LOAD CELLS
V-117
TO PRODUCT DRUMS
VENT / EQUALISE
TO VACUUM (TBC)
VT-101
VACUUM TRAP
COOLING TBC
DN25-VG-109
VP-101
VACUUM PUMP
DN25-VG-110
EXHAUST TO
SAFE LOCATION
V-114
DR
N₂ SUPPLY
PRESSURE TBC
NRV-102
V-112
DN15-NG-111
PV-102
FO
V-113
FROM PIC-102
HV-110
VAC. BREAK
TZ
110
TZ-110 REC. (HOLD): BLOCKS HV-110
WHILE POT (TT-101B) > 150 °C
LEGEND
HAND VALVE (BLOCK / DRAIN), V-1nn
CHECK VALVE, FLOW →, NRV-1nn
GLOBE (BYPASS) VALVE
CONTROL VALVE, DIAPHRAGM; FO / FC = FAIL OPEN / CLOSED
ON/OFF VALVE, SOLENOID-PNEUMATIC (S)
THREE-WAY DIVERTER VALVE
RELIEF VALVE (DASHED = RECOMMENDED, HOLD)
ORIFICE FLOW ELEMENT
CENTRIFUGAL PUMP (MOTOR NOT SHOWN)
FIELD INSTRUMENT (TRANSMITTER / ELEMENT)
DCS FUNCTION (SHARED DISPLAY / CONTROL)
SIS-100 FUNCTION (TRIP)
RECOMMENDED INSTRUMENT (DASHED, HOLD)
INTERLOCK LOGIC (DIAMOND)
INSTRUMENT SIGNAL (ELECTRIC / SOFTWARE)
PROCESS LINE, FLOW DIRECTION
UTILITY / DRAIN / VENT LINE
CONNECTION (TEE)
LINE NUMBER DNxx-SVC-1nn (SIZES PRELIMINARY, TBC)
PV PROCESS VAPOUR · PL PROCESS LIQUID · VG VACUUM GAS
NG NITROGEN · HO HOT OIL · TW TEMPERED WATER · CW COOLING WATER
EQUIPMENT LIST (BOTH SHEETS)
TAG
SERVICE
DATA (DESIGN CASE)
C-101
PACKED COLUMN
20 STAGES, ID 150 mm TBC
D-101
BATCH STILL (POT)
150 L, CHARGE 110 L
D-102
REBOILER, HOT OIL
DUTY 3.0 kW
E-103
OVERHEAD CONDENSER
2.37 kW, TW 60 °C
D-104
REFLUX DRUM
4 L; 50 % = 1.74 kg
P-104
REFLUX / DISTILLATE PUMP
DRAW 0–70 kg/h
VT-101
VACUUM TRAP
SIZE / COOLING TBC
VP-101
VACUUM PUMP
TOP 160 mbar a
TK-201
OFF-CUT RECEIVER
11.1 kg (CAMPAIGN A)
TK-202
PRODUCT RECEIVER
34.7 kg (CAMPAIGN A)
HE-101
HOT-OIL HEATER (PID-002)
12 kW ELECTRIC
P-101
HOT-OIL PUMP (PID-002)
125 kg/h AT DESIGN
E-104
HOT-OIL COOLER (PID-002)
COOL-DOWN ONLY
P-108
TEMP.-WATER PUMP (PID-002)
1.2 m³/h, 60 °C
TK-102
HOT-OIL EXP. TANK
RECOMMENDED, HOLD
GENERAL NOTES
1. ALTERNATIVE VERSION TO EPC STANDARD. THE SCREEN P&ID VBD-V1-PID-001 (P&ID TAB, TOP) STAYS THE REFERENCE FOR THE DCS, THE DECKS AND THE EXERCISES.
2. DESIGN CASE (OTS MODEL, NOISE OFF, START OF CAMPAIGN AT TOTAL REFLUX): TOP 160 mbar a (PIC-102), POT 170.9 mbar a, COLUMN ΔP 10.9 mbar, FLOODING 61 %;
POT DUTY 3.0 kW (JIC-101); HOT OIL 290 °C (TIC-107); TEMPERED WATER 60 °C, 1.2 m³/h; CHARGE 110 L = 95.7 kg FAME (89 % LEVEL HOT, 133 L AT 255 °C).
3. TOTAL REFLUX: TI-104 192.4, TI-103 193.3, TI-102 239, POT 255.9 °C; OVERHEAD 31.7 kg/h (MW 214); E-103 LOAD 2.37 kW; REFLUX 31.8 kg/h.
4. CAMPAIGN A: OFF-CUT R 15 → TK-201, PRODUCT CUT R 10 → TK-202 (C16:0 ≥ 99.0 wt %). SWITCH 307 min, END 907 min; TK-201 11.1 kg, TK-202 34.7 kg,
RECOVERY 80.7 %; RESIDUE 45.5 kg STAYS IN D-101. MASS BALANCE CLOSES TO 0.002 % (eng_check.py).
5. VAPOUR-PRESSURE ANCHORS, ΔHv, PACKING CAPACITY, CONDENSER UA, POT HEAT LOSS ARE ASSUMED IN THE MODEL (TBC).
6. LINE SIZES PRELIMINARY (TBC). OVERHEAD DN40: 7.6 m/s, 0.12 mbar/m (DN25 WOULD GIVE 17.9 m/s, 1.1 mbar/m). LIQUID LINES AT MINIMUM SIZE.
7. ALL VESSELS SEE VACUUM: DESIGN FV / 1.0 barg ASSUMED (HOLD); MATERIALS TBC. ESTER LINES TRACED / INSULATED ABOVE 45 °C (ESTERS FREEZE 30–38 °C), TBC.
8. PRESSURE AND LEVEL INSTRUMENTS C/W ROOT AND TEST VALVES (TYP., NOT SHOWN). PUMP MOTORS AND CASING DRAINS NOT SHOWN.
9. NEW TAGS ON THIS SET: V-101…V-122, NRV-101/102/104/108/112, FT-101, TT-101, LINE NUMBERS. ALL OTHER TAGS ARE THE OTS TAGS, UNCHANGED.
10. CHARGE METHOD, RECEIVER VENT / EQUALISING LINE, VT-101 COOLING AND DRAINING: TBC.
INSTRUMENT AND SAFETY NOTES
11. FIELD TRANSMITTERS (CIRCLE) ARE DRAWN SEPARATE FROM DCS FUNCTIONS (BAR) AND SIS-100 FUNCTIONS (SQUARE). AS IN THE MODEL, PSHH-102 SHARES PT-102
AND LSLL-101 SHARES LT-101 WITH THE DCS; TSHH-101 HAS ITS OWN ELEMENT TE-101B.
12. SIS-100 TRIPS (DELAY): TSHH-101 > 290 °C (5 s) · PSHH-102 > 300 mbar (5 s, RUN) · FSLL-108 < 0.36 m³/h (10 s, RUN) · LSLL-101 < 20 % (5 s, RUN) ·
TSHH-107 > 330 °C (5 s) · HS-100. ACTIONS, PERMISSIVES AND RESET: INTERLOCK SCHEDULE ON VBD-PID-002.
13. LSLL-104 < 5 % FOR 5 s STOPS P-104 (PUMP PROTECTION IN THE BPCS, NOT A SIF).
14. FAIL POSITIONS: PV-102 FO (N₂ BLEED OPEN; TOP SETTLES ≈ 300 mbar = PSHH-102), FV-104 FO (REFLUX KEPT), FV-105 FC (NO DRAW-OFF),
XV-101 / TV-101 FC (VBD-PID-002). XV-107 STAYS PUT AND HV-105 FO: ASSUMED (TBC).
15. PIC-102 → PV-102. LIC-104 → RY-104 → SET POINTS OF FIC-104 (R/(R+1)) AND FIC-105 (1/(R+1)). HS-107 → XV-107: CLOSED / TK-201 / TK-202; A TRIP SETS CLOSED.
16. HV-110 N₂ VACUUM BREAK ONLY WITH THE POT BELOW 150 °C (PROCEDURE TODAY).
17. DASHED ITEMS ARE RECOMMENDED BY THE HAZOP AND SAFETY-LAYERS TABS AND DO NOT EXIST: PSV-101, RD-102 + PSV-102, PT-102B, LT-101B, TZ-110 (HOLD).
RELIEF SET 1.0 barg ASSUMED; SIZE TO API 520/521 ONCE MAWP AND N₂ REGULATOR PRESSURE ARE KNOWN (HOLD).
18. RO-102 (N₂), TSV-103 (E-103 WATER SIDE), AT-102 (O₂) AND FA-101 ARE FURTHER RECOMMENDATIONS IN THE SAFETY-LAYERS TAB, NOT DRAWN.
REV
DESCRIPTION
DATE
—
VBD-V1-PID-001 A (SCREEN): CURRENT, DCS/DECKS
—
A
ALTERNATIVE VERSION, EPC STANDARD
12-OCT-26
CLIENT: DEPARTMENT OF CHEMICAL ENGINEERING,
FACULTY OF ENGINEERING, CHULALONGKORN UNIVERSITY
VACUUM BATCH DISTILLATION VER 1 · OTS
P&ID — VACUUM BATCH DISTILLATION C-101
· ALTERNATIVE VERSION
DRAWN:
Apinan Soottitantawat
CHK'D: --
APP'D: --
DATE: 12-OCT-26
DWG NO.
VBD-PID-001
REV
A
SCALE
N.T.S.
SHEET
1 OF 2
ALTERNATIVE VERSION · EPC STANDARD
REFERENCE: SCREEN P&ID VBD-V1-PID-001
SHEET 1 OF 2 · PROCESS: C-101, D-101, D-102, OVERHEAD, RECEIVERS, VACUUM