## Slide 1
HE-101
HOT-OIL HEATER
12 kW ELECTRIC, ELEMENT STEPS TBC
DESIGN OUTPUT 4.04 kW (33.7 %)
TO D-102 TUBE SIDE
ON VBD-PID-001
DN25-HO-116
TT
107
TIC
107
TT
107B
TSHH
107
TE-107B
V-104
P-101
HOT-OIL PUMP
NRV-101
V-105
S
FC
XV-101
V-106
FC
TV-101
V-107
V-108
BYPASS
FT
101
NEW TAG
JIC
101
Q = FT-101 × cp × (TT-107 − TT-108)
SP 3.0 kW (DESIGN)
TSV-101 REC. (HOLD)
TO TK-102, SET TBC
POWER
SIS-100
CONTACTOR
TRIP
HS
100
ESD
INPUTS ALSO FROM VBD-PID-001: TSHH-101, PSHH-102, LSLL-101
OUTPUTS ALSO (SOFTWARE): JIC-101 / TIC-107 / TIC-101 → MAN, XV-107 → CLOSED
FROM D-102 TUBE SIDE
ON VBD-PID-001
DN25-HO-117
TT
108
TI
108
RETURN 255.6 °C
E-104
HOT-OIL COOLER (COOL-DOWN)
HV-104
CWS
CWR
DN15-CW-120
V-109
DR
V-118
DR
TK-102
EXP. TANK
REC. (HOLD)
VENT / N₂ BLANKET
SIZE FOR 30 → 330 °C
TEMPERED-
WATER UNIT
60 °C, TCV INCL.
PACKAGE BY
OTHERS (TBC)
TO E-103
ON VBD-PID-001
DN25-TW-118
V-119
P-108
TEMPERED-WATER PUMP
NRV-108
V-120
FT
108
FI
108
FSLL
108
→ SIS-100
TT
109
TI
109
FO*
HV-105
HIC
105
FT
108B
REC. (HOLD): OWN SENSOR
FOR FSLL-108
FROM E-103
ON VBD-PID-001
DN25-TW-119
V-121
DR
V-122
VENT
* FAIL POSITION ASSUMED (TBC)
E-103 WATER SIDE: TSV-103 RECOMMENDED IF IT CAN BE BLOCKED IN (SAFETY-LAYERS TAB, NOT DRAWN)
INTERLOCK SCHEDULE · SIS-100 AND P-104 PUMP INTERLOCK (FROM THE OTS MODEL)
X = ACTION ON TRIP. SETTINGS FROM K.trip*; DELAYS FROM sisStep [5, 5, 10, 5, 5] s; ACTIONS FROM sisTrip.
ITEM
TAG
SENSOR
CAUSE
SETTING
DELAY
ACTIVE
TV-101 SHUT
(JIC-101
MAN 0 %)
HE-101 OFF
(TIC-107
MAN 0 %)
XV-101
CLOSED
TIC-101
→ MAN
XV-107 →
CLOSED
(TOT. REFL.)
P-104
STOP
FIRST-OUT
+ ALARM
RESET
I-1
TSHH-101
TE-101B / TT-101B (OWN)
POT D-101 TEMPERATURE HIGH-HIGH
> 290 °C
5 s
ALWAYS
X
X
X
X
X
X
BLOCKED UNTIL POT < 290 °C
I-2
PSHH-102
PT-102 (SHARED, PIC-102)
COLUMN TOP PRESSURE HIGH-HIGH
> 300 mbar
5 s
HEATING ARMED
X
X
X
X
X
X
ANY TIME; RE-ARM NEEDS PERMISSIVES
I-3
FSLL-108
FT-108 (SHARED, FI-108)
TEMPERED WATER TO E-103 LOW-LOW
< 0.36 m³/h
10 s
HEATING ARMED
X
X
X
X
X
X
ANY TIME; RE-ARM NEEDS PERMISSIVES
I-4
LSLL-101
LT-101 (SHARED, LI-101)
POT D-101 LEVEL LOW-LOW
< 20 %
5 s
HEATING ARMED
X
X
X
X
X
X
ANY TIME; RE-ARM NEEDS PERMISSIVES
I-5
TSHH-107
TE-107B / TT-107B (OWN)
HOT-OIL SUPPLY TEMPERATURE HIGH-HIGH
> 330 °C
5 s
ALWAYS
X
X
X
X
X
X
BLOCKED UNTIL OIL < 330 °C
I-6
HS-100
PUSH-BUTTON (DCS / SIS)
MANUAL EMERGENCY STOP
PUSH
0 s
ALWAYS
X
X
X
X
X
X
RESET, THEN RE-ARM
I-7
LSLL-104
LT-104 (SHARED, LIC-104)
REFLUX DRUM LEVEL LOW-LOW (BPCS, NOT A SIF)
< 5 %
5 s
P-104 RUNNING
X
ALARM
RESTART P-104 IN THE FIELD
REC.
TZ-110
TT-101B (REC., HOLD)
N₂ VACUUM BREAK HV-110 WITH POT > 150 °C
> 150 °C
—
ALWAYS
BLOCKS HV-110 (NOT IN MODEL)
PERMISSIVES TO ARM HEATING (armPermissives, ALL REQUIRED): VP-101 RUNNING AND PIC-102 < 250 mbar · P-108 RUNNING AND FI-108 ≥ 0.6 m³/h · LI-101 > 30 % ·
P-101 RUNNING · TIC-107 < 320 °C · HV-110 CLOSED. ARMING OPENS XV-101 AND ENABLES HE-101. OPERATOR DISARM: XV-101 CLOSED, HE-101 OFF.
VP-101, P-108, P-101 AND P-104 KEEP RUNNING ON A SIS TRIP: VACUUM, CONDENSER AND REFLUX STAY ON SO THE COLUMN COOLS UNDER TOTAL REFLUX.
LEGEND
HAND VALVE (BLOCK / DRAIN), V-1nn
CHECK VALVE, FLOW →, NRV-1nn
GLOBE (BYPASS) VALVE
CONTROL VALVE, DIAPHRAGM; FO / FC = FAIL OPEN / CLOSED
ON/OFF VALVE, SOLENOID-PNEUMATIC (S)
THREE-WAY DIVERTER VALVE
RELIEF VALVE (DASHED = RECOMMENDED, HOLD)
ORIFICE FLOW ELEMENT
CENTRIFUGAL PUMP (MOTOR NOT SHOWN)
FIELD INSTRUMENT (TRANSMITTER / ELEMENT)
DCS FUNCTION (SHARED DISPLAY / CONTROL)
SIS-100 FUNCTION (TRIP)
RECOMMENDED INSTRUMENT (DASHED, HOLD)
INTERLOCK LOGIC (DIAMOND)
INSTRUMENT SIGNAL (ELECTRIC / SOFTWARE)
PROCESS LINE, FLOW DIRECTION
UTILITY / DRAIN / VENT LINE
CONNECTION (TEE)
LINE NUMBER DNxx-SVC-1nn (SIZES PRELIMINARY, TBC)
PV PROCESS VAPOUR · PL PROCESS LIQUID · VG VACUUM GAS
NG NITROGEN · HO HOT OIL · TW TEMPERED WATER · CW COOLING WATER
RECOMMENDED ADDITIONS (DASHED, NOT EXISTING, HOLD)
PSV-101 C-101 TOP · RD-102 + PSV-102 POT (PID-001)
TSV-101 HOT-OIL SIDE OF D-102 → TK-102 (PID-002)
TK-102 HOT-OIL EXPANSION TANK, N₂ BLANKET (PID-002)
PT-102B, LT-101B (PID-001), FT-108B (PID-002):
OWN SENSORS FOR PSHH-102, LSLL-101, FSLL-108
TZ-110 HV-110 INTERLOCK, POT > 150 °C (PID-001)
SOURCE: HAZOP R02/R03/R13 AND SAFETY-LAYERS REGISTER
NOTES (HOT OIL AND TEMPERED WATER)
1. PART OF THE ALTERNATIVE VERSION (EPC STANDARD). GENERAL NOTES, EQUIPMENT LIST AND PROCESS SIDE: VBD-PID-001.
2. HOT OIL: SUPPLY 290 °C (TIC-107), RETURN 255.6 °C (ΔT 34.4 K). TV-101 36.7 % OPEN GIVES mcp 0.087 kW/K = 125 kg/h AT cp 2.5 kJ/kg K (ASSUMED);
TV-101 WIDE OPEN ≈ 1080 kg/h. HE-101 4.04 kW = POT DUTY 3.00 kW + LOOP LOSS 1.04 kW (BALANCE CLOSES TO 0.000 kW).
3. OIL GRADE, FLASH POINT, LOOP VOLUME, P-101 HEAD, HE-101 ELEMENT STEPS: TBC. HE-101 HAS POWER ONLY WITH P-101 RUNNING (MODEL; CONFIRM).
4. JIC-101 DUTY = FT-101 × cp × (TT-107 − TT-108). FT-101 IS A NEW TAG FOR THE FLOW THE MODEL USES; METER TYPE AND RANGE TBC.
5. TEMPERED WATER 60 °C, 1.2 m³/h; ΔT ACROSS E-103 1.7 K AT 2.37 kW. KEEP SUPPLY ABOVE 45 °C (TI-109 L ALARM): ESTERS FREEZE AT 30–38 °C.
6. E-104 / HV-104 ONLY FOR COOL-DOWN (SHUTDOWN PROCEDURE). COOLING-WATER CONDITIONS TBC.
7. DCS ALARMS (OTS): TIC-107 H 315 °C · JIC-101 H 5.0 kW · FI-108 L 0.6 m³/h · TI-109 L 45 / H 80 °C · TIC-101 H 280 °C.
8. LINE SIZES PRELIMINARY (TBC): HOT OIL DN25 = 0.72 m/s AT 1080 kg/h (ρ 750 ASSUMED); TEMPERED WATER DN25 = 0.60 m/s.
INTERLOCK NOTES
9. A TRIP SETS JIC-101 AND TIC-107 TO MAN 0 % (TV-101 SHUT, HE-101 OFF), TIC-101 TO MAN, XV-107 TO CLOSED; SIS-100 LEAVES RUN SO XV-101 CLOSES.
10. PSHH-102, FSLL-108 AND LSLL-101 ACT ONLY WHILE HEATING IS ARMED. TSHH-101 AND TSHH-107 ACT ALWAYS AND BLOCK THE RESET WHILE ABOVE THE SETTING.
11. SIS-100 DE-ENERGISES TO TRIP; XV-101 AND TV-101 FAIL CLOSED; HE-101 CONTACTOR OPENS. FIRST-OUT SHOWN ON THE SIS FACEPLATE.
12. SHARED SENSORS (SAFETY-LAYERS TAB GAPS): PT-102, FT-108, LT-101 SERVE CONTROL / ALARM AND TRIP. OWN SENSORS ARE RECOMMENDED (HOLD).
13. AIR INGRESS (HIGH RISK IN THE HAZOP) HAS NO SIF: TZ-110 AND AN O₂ ANALYSER AT-102 ARE RECOMMENDED (HOLD).
14. SIL TARGETS, PROOF TESTS AND RESPONSE TIMES: SRS OF SIF TAB. CAUSE AND EFFECT: C&E MATRIX VBD-IN-CE-001.
REV
DESCRIPTION
DATE
—
VBD-V1-PID-001 A (SCREEN): CURRENT, DCS/DECKS
—
A
ALTERNATIVE VERSION, EPC STANDARD
12-OCT-26
CLIENT: DEPARTMENT OF CHEMICAL ENGINEERING,
FACULTY OF ENGINEERING, CHULALONGKORN UNIVERSITY
VACUUM BATCH DISTILLATION VER 1 · OTS
P&ID — VACUUM BATCH DISTILLATION C-101
· ALTERNATIVE VERSION
DRAWN:
Apinan Soottitantawat
CHK'D: --
APP'D: --
DATE: 12-OCT-26
DWG NO.
VBD-PID-002
REV
A
SCALE
N.T.S.
SHEET
2 OF 2
ALTERNATIVE VERSION · EPC STANDARD
REFERENCE: SCREEN P&ID VBD-V1-PID-001
SHEET 2 OF 2 · HOT-OIL SKID, TEMPERED WATER, SIS-100, INTERLOCK SCHEDULE